Features

- Wi-Fi Compliant with IEEE 802.11g and IEEE 802.11b Standards

- Supports Ad-Hoc (Peer-to-Peer) Mode or Infrastructure (AP-Client) Mode

- Supports Super G technology Data Rate up to 108Mbps

- Dynamic Data Rate Scaling at 54, 48, 36, 24, 18, 12, 9 and 6Mbps for 802.11g

- Dynamic Data Rate Scaling at 11, 5.5, 2 and 1Mbps for 802.11b

- Maximum Reliability, Throughput and Connectivity with Automatic Data Rate Switching

- Compatible with Windows 98SE/ME/2000/XP/2003

- Supports 64/128/152-bit WEP, WPA, WPA-PSK without Performance Degradation

- Low Interference and High Susceptibility Guarantee Reliable Performance

- Range of 35~100 meters indoor, 100~300 meters outdoor (depends on the environment)

- Simple User Setup & Diagnostics Utilities

- 3-Year Warranty

Specifications

| Hardware |
| --- |
| Interface | USB 2.0, 1.1 Compliant |
| Standards | IEEE802.11b and IEEE 802.11g |
| Power Consumption | 450mA @ 5V DC |
| Supported OS | Windows 98SE/ME/2000/XP/2003 |
| Dimensions (LxWxH) | 95 x 22 x 10 mm (3.7 x 0.87 x 0.4 inches) |
| Weight | 28 g (1 oz.) |
| Temperature | Operating: 0( ~ 40( C (32( ~ 104( F) Storage: -20( ~ 70( C (-4( ~ 158( F) |
| Humidity | 10% ~ 90%max (Non-condensing) |
| Emissions | FCC, CE |
| Wireless |
| Module Technique | 802.11b: CCK (11 and 5.5Mbps), DQPSK (2Mbps), DBPSK (1Mbps) 802.11g: OFDM |
| Frequency | 2.412 ~ 2.484 GHz |
| Media Access Protocol | CSMA/CA |
| Data Rate (auto fallback) | 802.11b: 11Mbps, 5.5Mbps, 2Mbps, and 1Mbps 802.11g: 54Mbps, 48Mbps, 36Mbps, 24Mbps, 18Mbps, 12Mbps, 9Mbps and 6Mbps Super G: 108Mbps |
| Transmit Power | 802.11b: 18dBm (typical) @ 11Mbps 802.11g: 15dBm (typical) @ 54Mbps |
| Receiving Sensitivity | 802.11b: -82 dBm @ 11Mbps 802.11g: -70 dBm @ 54Mbps |
| Encryption | 64/128/152-bit WEP (Hex & ASCII), WPA-PSK, WPA/ 802.1x: (EAP-TLS, EAP-TTLS, PEAP(EAP-GTC), PEAP(EAP-MSCHAP V2), LEAP) |
| Channels | 1~11 (US), 1~13 (EU) |

Package Contents				Related Products

- TEW-444UB					- TEW-441PC

- Utility & Driver CD-ROM			- TEW-443PI

- Multi-Language Quick Installation Guide	- TEW-450APB

- 1 x USB 2.0 Cable (102mm/4inches)		- TEW-452BRP

To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

## Sales: sales@trendware.com • Support: techsupport@trendware.com

Tech Support Hotline: (310)626-6252

Official Site: www.TRENDNET.com

# Text boxes

New Implements

- New Logo on Housing / Packaging

- RoHS version hardware

- Microsoft Windows XP Certified

- Added WPA-PSK/802.1x Encryption

- Free McAfee Utility Trial Version

# 108Mbps 802.11g Wireless USB 2.0 Adapter

TEW-444UB 802.11g USB 2.0 Wireless adapter provides wireless connectivity with 802.11g, or 802.11b networks and an easy-to-install, backward compatible interface to bring the best wireless solution for desktop/mobile workstations. The TEW-444UB can reach blazing speeds of 108Mbps. It also dynamically encrypts wireless transmissions with WPA-PSK.

#### TEW-444UB (v1.1R)_