Features

- Wi-Fi Compliant with IEEE 802.11g and 802.11b Devices

- 4 x 10/100Mbps Auto-MDIX LAN Ports and 1 x 10/100Mbps WAN Port (Internet)

- Supports Cable/DSL Modems with Dynamic IP, Static IP, PPPoE, PPTP, or L2TP Connection Types

- Supports Super G and XR (eXtended Range) Technology Data Rate up to 108Mbps (AP Mode Only)

- DHCP Server Feature Allocates up to 253 Client IP Addresses

- Supports 64/128-bit WEP, WPA and WPA2 Encryptions

- Supports MAC Address, IP, URL, Protocol Filters, Domain Blocking, and Firewall rules Access Controls

- Traffic Control with Virtual Server and DMZ

- Provides Additional Security with SPI / NAT firewall and Attack Alert via emails

- Provides Additional Security of Enable/Disable SSID, Password Protection

- Supports Static and Dynamic Routing

- Supports IPSec and PPTP VPN Pass-Through Sessions

- Flash Memory for Firmware Upgrade, Save/Restore Settings, and Traffic Log

- Easy Management via Web Browser (HTTP) and Remote Management

- Compliant with Windows 95/98/NT/2000/XP, Linux and Mac OS

- Range for Indoor of 30 ~ 50 meters (depends on the environment)

- Range for Outdoor of up to 200 meters (without XR), up to 450 meters (with XR) (depends on the environment)

- 3-Year Warranty

Specification

| Hardware |
| --- |
| Standards | Wired: IEEE 802.3 (10Base-T), IEEE 802.3u (100Base-TX), ANSI/IEEE 802.3 Auto Negotiation Wireless: IEEE 802.11b (11Mbps), IEEE 802.11g (54Mbps) |
| WAN | 1 x 10/100Mbps Auto-MDIX Port (Internet) |
| LAN | 4 x 10/100Mbps Auto-MDIX Port |
| Connection Type | Dynamic IP, Static (Fixed) IP, PPPoE, PPTP, L2TP |
| Supported Protocols | 802.3u: 10/100Mbps Fast Ethernet, IP v4, UDP, ICMP, TCP Secure: PAP, CHAP, Network Timing Protocol, DHCP, Dynamic DNS, PPPoE, PPTP, L2TP, UPnP |
| LED Indicator | System, Link, ACT, WAN, WLAN |
| Dual Diversity Antenna | 1 x Internal Printed Antenna 1 x 2dBi External Detachable Dipole Antenna (Female Reverse SMA Connector) |
| Dimension (L x W x H) | 155 x 110 x 30 mm (6 x 4.3 x 1.2 inches) |
| Weight | 226g (8 oz.) |
| Temperature | Operation: 0(~ 55(C (32(F~ 131(F) Storage: -10(~ 70(C (14(F~ 158(F) |
| Humidity | Max. 95% (Non-Condensing) |
| Power Adapter | 5V DC, 2.5A External Power Adapter |
| Certification | FCC & CE |
| Wireless |
| Frequency | 2.412 to 2.484GHz (Industrial Scientific Medical Band) |
| Module Technique | 802.11b: CCK (11 and 5.5Mbps), DQPSK (2Mbps), DBPSK (1Mbps) 802.11g: OFDM |
| Media Access Protocol | CSMA/CA with ACK |
| Security | 64/128-bit WEP, WPA(EAP)/WPA-PSK, WPA2(EAP)/WPA2-PSK |
| Transmit Power | 15 dBm ( 2dBm |
| Data Rate | 802.11b: 11Mbps, 5.5Mbps, 2Mbps, and 1Mbps 802.11g: 54Mbps, 48Mbps, 36Mbps, 24Mbps, 18Mbps, 12Mbps, 9Mbps and 6Mbps Super G: 108Mbps |
| Receiving Sensitivity | 11Mbps: -85 dBm @ 8% PER (typical) 54Mbps: -70 dBm @ 10% PER (typical) |
| Channels | 11 Channels (US), 13 Channels (EU) |

Package Contents				Related Products

- TEW-452BRP					- TEW-441PC

- Multi-Language QIG				- TEW-443PI

- CD-ROM (User’s Guide)			- TEW-444UB

- Power Adapter (5V DC, 2A)			- TEW-450APB

- RJ-45 Cable (1.5m)

To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

Sales: sales@trendnet.com • Support: techsupport@trendnet.com

www.TRENDnet.com

# Text boxes

108Mbps 802.11g Wireless Firewall Router

The Wireless AP/Router is the cornerstone of your IEEE 802.11g wireless network. Capable of speeds of up to 108Mbps, the TEW-452BRP built-in AP facilitates seamless wireless communication between your devices. The unit’s router enables you to share a single Internet account with multiple users, while its 10/100Mbps 4-port switch gives you the flexibility to support wired Ethernet connections. With WEP and WPA-compliant encryption protecting your information, you’ll be able to share files, Internet connections, and other resources with the peace of mind you deserve.  Other security features include a SPI firewall.

TEW-452BRP (B1.0R)

New Implements

- New Compact Housing

- Added WPA2 & WPA2-PSK support