Features

- Wi-Fi Compliant with IEEE 802.11g / 802.11b Wireless Devices

- One 2dBi Detachable Antenna with Reverse SMA Connector

- High-Speed Wireless Access Point with up to 108Mbps Connection

- Supports Access Point, AP Client/Repeater and Bridge (PTP or PTMP up to 8 units) Modes

- 64/128/152-bit Wired Equivalent Privacy (WEP) with HEX or ASCII key

- Supports WPA/WPA-PSK, AES and TKIP

- Allows 802.1x and Non-802.1x Clients Running Simultaneously

- Supports 802.1Q Tag VLAN, allowing traffic from different sources to be segmented

- Supports Radius-based MAC address authentication and MAC Address Filter

- Supports Client to Client Communication Prevention per ESSID, Wireless Separation

- Multiple Security Profiles (max active 4), SSID Isolation and UAM (Universal Access Method)

- Supports  Wireless Separations (between clients)and Worldwide Wireless Mode (802.11d) Standard

- Detects Rogue Access Points with Logs

- Easy Configuration with Web Browser (HTTP/HTTPS) or Telnet

- Flash Memory for Firmware Upgrade

- Range for 802.11b: up to 35~60 meters indoor, 300 meters outdoor (depends on the environment)

- Range for 802.11g: up to 20 meters indoor, 50 meters outdoor (depends on the environment)

- 3-Year Warranty

Specifications

| Hardware |  |
| --- | --- |
| Standards | Wired: IEEE 802.3 (10Base-T), IEEE 802.3u (100Base-TX) , IEEE 802.3af PoE Wireless: IEEE 802.11b (11Mbps), IEEE 802.11g (54Mbps), IEEE 802.1x, IEEE 802.11d |
| LED Indicators | Power, Status, LAN and WLAN |
| Console Port | RS232 Port (DB9) |
| Protocols | TCP/IP, NetBEUI, ARP, DHCP Client, HTTP, NTP, RADIUS, WINS, Telnet, FTP, HTTPs, SSL |
| CPU/Radio/RAM/Flash | Atheros 2312/ Atheros 2112/ 8Mbytes/ 2Mbytes |
| Client Support | DHCP Client, WINS Client, Radius Client |
| Power Source | 24V DC, 500mA External Power Adapter or PoE Connection |
| Dimensions (LxWxH) | 141 x 100 x 27 mm (5.5 x 3.9 x 1.06 inches) (without antennas) |
| Weight | 0.35 kg. (12.5 oz.) |
| Temperature | Operating: 0(~ 40(C (32(F~ 104(F) Storage: -10(~ 70(C (14(F~ 158(F) |
| Humidity | Max. 95% (non-condensing) |
| Certification | FCC, CE |
| Wireless |  |
| Module Technique | 802.11b: CCK, DQPSK, DBPSK ; 802.11g: OFDM |
| Frequency Range | 2.4 ~ 2.497 GHz |
| Modes | Access Point, AP Client/Repeater, Bridge (PTP or PTMP) |
| Data Rate (auto fallback) | 802.11b: 11Mbps, 5.5Mbps, 2Mbps, and 1Mbps 802.11g: 54Mbps, 48Mbps, 36Mbps, 24Mbps, 18Mbps, 12Mbps, 9Mbps and 6Mbps |
| Channels | 1~14 Channels (Universal Support) |
| Security | 64/128/152-bit (WEP), 802.1x WPA-PSK or WPA-802.1x (TKIP, AES, EAP-MD5, EAP-TLS, EAP-TTLS, PEAP) |
| Management | Web Browser (HTTP or HTTPS); SNMP V2, V2C; Telnet & CLI |
| Antenna | 1 x 2dBi External Detachable Dipole Antenna with Female Reverse SMA connector |
| Output Power | Adjustable: Full (18dBm), Half (15dBm), Quarter (12dBm), Eighth (9dBm), Minimum (6dBm) |
| Receiving Sensitivity | 11Mbps 10 – 5 BER @ -86 dBm (typical) 54Mbps 10 – 5 BER @ -71 dBm (typical) 108Mbps 10 – 5 BER @ -68 dBm (typical) |

### TOP REASONS THE TEW-453APB IS THE LASTING TREND

| Easy Integration | Setup your own Wireless Hot Spot fast and easy. |
| --- | --- |
| Cost-Effectiveness | Saves on network cable installation fee and on-line charges. |
| Security | 64/128/152-bit WEP protect Access Point from unwanted wireless clients. |
| Traffic Control | Controls traffic with MAC Address Filter feature |

Package Contents				Related Products

- TEW-453APB				- TEW-441PC

- Multi-Language QIG			- TEW-443PI

- CD-ROM (User’s Guide)			- TEW-444UB

- Power Adapter

To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

### Sales: sales@trendware.com • Support: techsupport@trendware.com

Tech Support Hot Line: 1-310-626-6252

### Official Site: www.TRENDNET.com

# Text boxes

TEW-453APB

108Mbps 802.11g Hot-Spot Access Point

The TEW-453APB is a 108Mbps high speed 802.11g Wireless Access Point that offers advanced wireless security, network management, and Power-over-Ethernet capabilities.  Wireless security features include TKIP and AES algorithms for WPA, and also Radius based MAC authentication.  Features for network management include VLAN, SNMP support, System log support, and Rogue AP for extra security.

Hot-Spot Access Point Solution