Features

- Wi-Fi Compliant with IEEE 802.11a, 802.11g and IEEE 802.11b Standards

- Uses 5 GHz or 2.4 GHz Dual Band Design, which Complies with Worldwide Requirements

- Supports WDS Access Point, AP Client/Repeater Modes

- Supports Super AG and XR (eXtended Range) technology Data Rate up to 108Mbps (AP Mode Only)

- Dynamic Data Rate Scaling at 54, 48, 36, 24, 18, 12, 9 and 6Mbps for 802.11a/g

- Dynamic Data Rate Scaling at 11, 5.5, 2 and 1Mbps for 802.11b

- Supports ESSID Enable/Disable Feature to Increase Security

- Supports 64/128/152-bit Wired Equivalent Privacy (WEP)

- Supports WPA and WPA-PSK

- Easy Configuration with Web Browser and Flash Memory for Firmware Upgrade

- Compliant with Windows 95/98/NT/2000/XP/2003 Server, Linux and Mac OS

- Range of 30 ~ 100 meters Indoor (depends on the environment)

- Range of 50 ~ 300 meters Outdoor (depends on the environment)

- 3-Year Warranty

Specifications

| Hardware |  |
| --- | --- |
| Standards | Wired: IEEE 802.3 (10Base-T), IEEE 802.3u (100Base-TX) Wireless: IEEE 802.11a (54Mbps), 802.11b (11Mbps), IEEE 802.11g (54Mbps) |
| Interface | LAN : 1 x 10/100Mbps Auto-MDIX Port Reset button : Reset settings to factory default |
| LED Indicators | Power, Link/Act, Full/Col, 11a Link/Act, 11g Link/Act |
| Network Protocols | TCP/IP, NetBEUI, IPX/SPX |
| Power Source | 5V DC, 2.5A External Power Adapter |
| Dimensions (LxWxH) | 198 x 160 x 33 mm (7.8 x 6.3 x 1.2inches) |
| Weight | 0.7kg (1.54 lbs) |
| Temperature | Operating: 0(~ 40(C (32(F~ 104(F) Storage: -20(~ 60(C (-4(F~ 120(F) |
| Humidity | Max. 90% (Non-Condensing) |
| Certification | FCC, CE |
| Wireless |  |
| Module Technique | 802.11b: CCK (11 and 5.5Mbps), DQPSK (2Mbps), DBPSK (1Mbps) 802.11a/g: OFDM with BPSK, QPSK and 16/64-QAM Sub-Carrier Modulations |
| Frequency Range | 802.11a: UNI-Band 5.15 ~ 5.85 GHz (Subject to Local Regulations) 802.11b/g: ISM-Band 2.412 ~ 2.497 GHz |
| Antenna | 802.11a: 4dBi (Peak Gain); 802.11b/g: 2dBi (Peak Gain) 2 x Dual Band Diversity Detachable Antenna (Female Reverse SMA Connector) |
| Data Rate (auto fallback) | 802.11b: 11Mbps, 5.5Mbps, 2Mbps, and 1Mbps 802.11g: 54Mbps, 48Mbps, 36Mbps, 24Mbps, 18Mbps, 12Mbps, 9Mbps and 6Mbps Super AG: 108Mbps |
| Security | 64/128/152-bit WEP & WPA MAC Address Filter |
| Transmit Power | 802.11a: 16dBm (max) @ 16QAM R3/4 802.11b: 18dBm (typical) 802.11g: 16dBm (typical) |
| Receiving Sensitivity (802.11a/b/g) | 108Mbps 10 – 5 BER @ -69 dBm (Turbo Mode) 802.11a: 54Mbps 10 – 5 BER @ -67 dBm 802.11b: 11Mbps 10 – 5 BER @ -80 dBm 802.11g: 54Mbps 10 – 5 BER @ -65 dBm |
| Channels | 802.11a: Subject to Local Regulations 802.11b/g: 1~ 11 (US), 1~13 (EU) |

Package Contents				Related Products

- TEW-510APB				- TEW-501PC

- Multi-Language QIG			- TEW-503PI

- CD-ROM (User’s Guide)			- TEW-504UB

- Power Adapter (5V DC, 2.5A)                                    - TEW-511BRP

- RJ-45 Cable (1.5m)

To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

### Sales: sales@trendware.com • Support: techsupport@trendware.com

Tech Support Hot Line: 1-310-626-6252

### Official Site: www.TRENDNET.com

# Text boxes

TEW-510APB

108Mbps 802.11a+g Wireless Access Point

The TRENDnet TEW-510APB Dual Band Super A+G Access Point meets the growing demand for bandwidth intensive applications such as streaming media.  The TEW-510APB provides seamless integration to compatible 802.11a/b/g wireless clients for high-speed Internet access. The TEW-510APB secures wireless communication with WEP, WPA or MAC filtering and provides fast frames, frame bursting, frame compression, and dynamic turbo for Super A or Super G clients.

802.11a/g Wireless Networking Solution

* Due to European Wireless Regulations, Super A mode is not supported in the EU version.