Features

- Wi-Fi Compliant with IEEE 802.11n (draft) Standard

- Wi-Fi Compliant with IEEE 802.11g and IEEE 802.11b Standards

- Supports Infrastructure (AP-Client) Mode

- High-Speed up to 300Mbps Data Rate using IEEE 802.11n (draft) connection

- 3 detachable antennas to support MIMO high speed performance and great coverage

- Dynamic Data Rate Scaling from 300Mbps to 1Mbps

- Maximum Reliability, Throughput and Connectivity with Automatic Data Rate Switching

- Universal Wireless Connectivity for Seamless Roaming among 802.11b/g/n Networks

- Supports 64/128-bit WEP, WPA/WPA2 and WPA-PSK/WPA2-PSK

- Low Interference and High Susceptibility Guarantee Reliable Performance

- Compatible with Windows 2000/XP Operating Systems

- Easy User Setup & Diagnostics Utilities

- 3-Year Warranty

Specifications

| Hardware |
| --- |
| Interface | 32-Bit PCI Rev. 2.1/2.2/2.3 |
| Standards | IEEE 802.11b, IEEE 802.11g and IEEE 802.11n (draft) |
| LED Indicator | Power, Link |
| Power Consumption | Receive Mode: 600mA(max) ; Transmit Mode: 690mA(max) |
| Supported OS | Windows 2000/XP |
| Weight | 140g (5 oz) |
| Temperature | Operating: 0( ~ 40( C (32( ~ 104( F) Storage: -25( ~ 70( C (-13( ~ 158( F) |
| Humidity | 10% ~ 90%max (Non-condensing) |
| Emissions | FCC, CE |
| Wireless |
| Module Technique | 802.11b: CCK (11 and 5.5Mbps), DQPSK (2Mbps), DBPSK (1Mbps) 802.11g: OFDM with BPSK, QPSK and 16/64-QAM sub-Carrier modulations 801.11n: OFDM, 64-QAM, coding rate 5/6 |
| Antenna | 2 x 2dBi & 1 x 5dBi detachable antennas (Reverse SMA Connector) |
| Frequency | 2.412 ~ 2.484 GHz |
| Media Access Protocol | CSMA/CA |
| Data Rate (auto fallback) | 802.11b: 11Mbps, 5.5Mbps, 2Mbps, and 1Mbps 802.11g: 54Mbps, 48Mbps, 36Mbps, 24Mbps, 18Mbps, 12Mbps, 9Mbps and 6Mbps 802.11n (draft) : up to 300Mbps |
| Output Power | 802.11b: 18dBm (typical) 802.11g: 15dBm (typical) 802.11n (draft) : 14dBm (typical) with HT20 & HT40 |
| Receiving Sensitivity | 802.11b: -84dBm (typical) @ 11mpbs 802.11g: -72dBm (typical) @ 54Mbps 802.11n (draft) : -70dBm (typical) with HT40 |
| Encryption | 64/128-bit WEP (Hex & ASCII), WPA/WPA2, WPA-PSK/WPA2-PSK |
| Channels | 1~11 (US), 1~13 (EU) |

Related Products		Package Contents

- TEW-621PC			- TEW-623PI

- TEW-630APB			- Utility & Driver CD-ROM

- TEW-631BRP			- Multi-Language Quick Installation Guide

To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

## Sales: sales@trendware.com • Support: techsupport@trendware.com

Tech Support Hotline: (310)626-6252

Official Site: www.TRENDNET.com

# Text boxes

### 300Mbps Wireless N-Draft PCI Adapter

The 300Mbps Wireless N-Draft PCI Adapter allows you to connect wirelessly with supercharged speed, range and reliability. Wireless speeds increase up to 300Mbps when connecting to TRENDnet Wireless N-Draft access points or wireless routers. This 802.11n device seamlessly connects to your wireless network without performance degradation.

#### TEW-623PI (V1.0R)