Features

- Compatible with 2.4GHz 802.11b/g or 5GHz 802.11a wireless devices

- Detachable antenna base allows high gain antenna  to be optionally connected to Wi-Fi device avoiding cable loss/attenuation

- Magnetic base allows convenient and optimal relocation to wall or any metallic surface

- Serves as an indoor omni relocation antenna.

- Enhances wireless coverage and improve signal transmission and reception

- Adjustable antenna face can tilt up to 180° and rotate up to 360° for optimal performance

- Easy-to-install wall and ceiling mount

- No configuration or installation software required

- 3-Year Warranty

Specifications

| Hardware |  |  |  |
| --- | --- | --- | --- |
| Frequency range | 802.11a: 4.9 ~5.875GHz 802.11b/g: 2.4 ~ 2.5GHz | Impedance | 50 Ohms |
|  |  | Connector | Reverse SMA Female |
| Gain | 802.11a: 7dBi 802.11b/g: 5dBi | Cable Length | 100cm (3.3ft.) |
|  |  | Temperature | -10°C ~ 55°C (14°F ~ 131°F) |
| VSWR | 2.0:1 | Humidity | 95% at 25°C |
| Polarization | Linear, vertical | Weight | Antenna: 40g (1.4oz.) Base: 82g (2.9oz.) |
| HPBW/ Horizontal | 360° |  |  |
| HPBW/ Vertical | 802.11a: 25° 802.11b/g: 35° | Dimension | Antenna: 217x28x14mm (8.5 x 1.1 x 0.55in.) Base: 80x58x 28mm (3.15 x 2.28 x1.1in.) |
| Power handling | 2W (cw) |  |  |

Radiation Patterns

Package Content 						Related Product

- TEW-AI07OB						- TEW-AI75O

- Mounting Kit						- TEW-AI86D

- Multi-Language User’s Guide				- TEW-AI86DB

To order please call: 888-326-6061; Sales: sales@trendnet.com

Support: support@trendnet.com; Tech Support Hotline: 888-777-1550

Official Site: www.trendnet.com

# Text boxes

TEW-AI75OB

Dual-band 802.11a/g 7/5dBi 
Indoor Omni Antenna with Mounting Base

TEW-AI75OB Omni Antenna provides more power and greater range for your wireless network. As an optional antenna for your IEEE 802.11b/g 2.4GHz or 802.11a 5GHz wireless network equipment, TEW-AI75OB will significantly improve signal strength and quality.  TEW-AI75OB will work with any brand of devices with reverse SMA male connector!

* This dBi gain does not factor cable loss. Performance estimations are for typical use; range will vary with site conditions.

* This Figure does not include cable loss

Antenna Solution with TEW-AI75OB