Features

- Compatible with 2.4GHz 802.11b/g or 5GHz 802.11a wireless devices.

- Works with any brand of wireless devices with reverse SMA male connector

- Serves as an indoor directional relocation antenna

- Enhances wireless coverage and improve signal transmission and reception

- Adjustable antenna face can tile up to 180° and rotate up to 360° for optimal performance.

- No configuration or installation software required

- 3-Year Warranty

Specifications

| Hardware |  |  |  |
| --- | --- | --- | --- |
| Frequency range | 802.11a: 4.9 ~5.875GHz 802.11b/g: 2.4 ~ 2.5GHz | Power Handling | 2W (cw) |
|  |  | Impedance | 50 Ohms |
| Gain | 802.11a: 8dBi 802.11b/g: 6dBi | Connector | Reverse SMA Female |
|  |  | Dimension | 128 x 85 x 15mm (5.04 x 3.35 x 0.59in.) |
| VSWR | 2.0:1 |  |  |
| Polarization | Linear, Vertical | Weight | 51g (4.5oz.) |
| HPBW/ Horizontal | 802.11a: 50° 802.11b/g:75° | Temperature | -10°C ~ 55°C (14°F ~ 131°F) |
| HPBW/ Vertical | 802.11a: 60° 802.11b/g:70° | Humidity | 95% at 25°C |

Radiation Patterns

Package Content 						Related Product

- TEW-AI86D						- TEW-AI86DB

- Multi-Language User’s Guide				- TEW-AI75O

- TEW-AI75OB

To order please call: 888-326-6061; Sales: sales@trendnet.com

Support: support@trendnet.com; Tech Support Hotline: 888-777-1550

Official Site: www.trendnet.com

# Text boxes

TEW-AI86D

Dual-Band 802.11a/g 8/6dBi 
Indoor Directional Antenna

TRENDnet’s TEW-AI06D Indoor Directional Antenna provides more power and greater range for your wireless network. As an optional antenna for your IEEE 802.11b/g 2.4GHz or 802.11a 5GHz wireless network equipment, TEW-AI86D will significantly improve signal strength and quality.  TEW-AI86D will work with any brand of device with reverse SMA male connector!!

* This dBi gain does not factor cable loss. Performance estimations are for typical use; range will vary with site conditions.

* This Figure does not include cable loss

Antenna Solution with TEW-AI86D