Features

- Compatible with 2.4GHz 802.11b/g wireless devices

- Serves as an indoor/outdoor point-to-point bridging antenna or a point-to-multi-point extended range antenna

- Weatherproof housing design for both indoor and outdoor applications

- Adjustable swivel mount for optimal performance

- Enhances wireless coverage and improve signal transmission and reception

- Boosts standard antenna power from a meager 2dBi to a respectable 9dBi

- Easy-to-install wall and pole mounting

- No configuration or installation software required

- 3-Year Warranty

Specifications

| Hardware |  |  |  |
| --- | --- | --- | --- |
| Frequency range | 2.4 ~ 2.5GHz | Impedance | 50 Ohms |
| Antenna Gain | 9dBi | Connector | N-Type Female |
| VSWR | 2.0:1 Max | Survival Wind Speed | 216 km/hr (134 miles/hr) |
| Polarization | Linear, Vertical | Radome Material | ABS |
| HPBW/ Horizontal | 60° | Dimension | 130 x 135 x 26mm (5.1 x 5.3 x 1.0in.) |
| HPBW/ Vertical | 60° |  |  |
| Front to Back Ratio | 15dB | Weight | 187g (6.6oz.) |
| Power Handling | 20W (cw) | Temperature | -40oC ~ 80oC (-40oF ~ 176oF) |

* Note: For optimal results in extending your wireless range with wireless antenna installations, we recommend that you consult a professional installer for site survey, safety precautions, and proper installation.

Patterns

Package Contents							Related Products

- TEW-AO09D							- TEW-AO08O

- Multi-Language Quick Installation Guide				- TEW-AO10O

- Mounting Guide							- TEW-AO14D

- Mounting Kit							- TEW-AO19O

- TEW-L202

- TEW-L208

- TEW-L406

- TEW-L412

To order please call: 888-326-6061; Sales: sales@trendnet.com

Support: support@trendnet.com; Technical Support: 866-845-3673

Official Site: www.trendnet.com

# Text boxes

TEW-AO09D Version V1.0R

9 dBi Indoor / Outdoor 
High-Gain Directional Antenna

TEW-AO09D Indoor / Outdoor Directional Antenna provides long distance point-to-point connectivity for your wireless network. As an optional antenna for your IEEE 802.11b/g 2.4GHz wireless network equipment, you can install it outdoor for long distance point to point connections, or install it in a building to blast through obstructions. Enjoy the benefits of wireless connectivity at greater distances and throughput throughout your indoor or outdoor wireless zone.

* This dBi gain does not factor cable loss. Performance estimations are for typical use; range will vary with site conditions.