Features

- Wi-Fi Compliant with 2.4GHz 802.11 b/g & 5GHz 802.11a Devices for extending wireless networks

- Reverse SMA Female to N-Type Male Connector.

- Optimal placement of your existing Wi-Fi Device permits you to maximize its wireless performance

- Flexible outer conductor allows the tightest bend radius available for any cable of similar size and performance

- Provides flexible Low-loss communication for wireless antenna

- 50dB RF Shielding is 10 dB greater than typical single shielded coax (40 dB).

- Multi-ply bonded outer foil conductor is rated conservatively at > 90 dB.

- Weatherproof cable design for outdoors exposure with best materials for UV resistance

- Polyethylene jacketed cable designed for outdoor use

- Easy and quick deployment into a WLAN environment

Specifications

| Construction | Electrical |
| --- | --- |
| Inner Conductor (Solid BC) | 0.044 in. (1.12 mm) | Cut-off Frequency | 39 GHz |
| Dielectric (Foam PE) | 0.116 in. (2.95 mm) | Velocity of Propagation | 83% |
| Outer Conductor (Aluminum Tape) | 0.121 in. (3.07 mm) | Dielectric Constant | 1.45 |
| Over Braid (Tinned Copper ) | 0.144 in. (3.66 mm) | Time Delay | 1.22 nS/ft (4.02 nS/m) |
| Jacket (PE) | 0.195 in. (4.95 mm) | Impedance | 50 ohms |
| Mechanical | Capacitance | 24.5 pF/ft (80.3 pF/m) |
| Bend Radius: Installation | 0.5 in. (12.7 mm) | Inductance | 0.061uH/ft (0.20 uH/m) |
| Bend Radius: Repeated | 2.0 in. (50.8 mm) | Shielding Effectiveness | > 90 dB |
| Bending Moment | 0.2 ft-lb (0.27 N-m) | DC Resistance Inner Conductor Outer Conductor | 5.36ohms/1000ft (17.6 ohms/km) 4.9 ohms/1000ft (16.1 ohms/km) |
| Weight | 0.022 lb/ft (0.03 kg/m) |  |  |
| Tensile Strength | 40 lb (18.2 kg) |  |  |
| Flat Plate Crush | 15 lb/in. (0.27 kg/mm) |  |  |
| Environment |  |  |
| Temperature | Operating: -40( C ~ 85(C (-40(F~185(F) Storage: -70( C ~ 85(C (-94(F~185(F) | Voltage Withstand | 1000 Volts DC |
|  |  | Jacket Spark | 3000 Volts RMS |
|  |  | Peak Power | 2.5 kW |

Package Contents							Related Product

- TEW-L202 / TEW-L206						- TEW-AO08O

- Weatherproof Tape						- TEW-ASAK

- User’s Guide							- TEW-L202/TEW-L208

- TEW-L406/TEW-L412

To order please call: 888-326-6061 • Sales: sales@trendnet.com

Support: support@trendnet.com • Tech Support Hotline: 1-888-777-1550

Official Site: www.trendnet.com

# Text boxes

Reverse RMA
 Female Connector

LMR200 Reverse SMA to N-Type Cable

The LMR200 Reverse SMA to N-Type Cable extends your wireless Antenna up to 2 or 8 meters to provide optimal placement for your antenna outdoors. Connect business networks from building to building wirelessly or provide wireless Internet access for hot spot applications!  This cable makes wireless communication possible by providing low loss communication between your access point and antenna.

TEW-L202/L208

Antenna Cable Solution

Interface

N-Type Male
 Connector