Features

- Wi-Fi Compliant with 2.4GHz 802.11 b/g & 5GHz 802.11a Devices for extending wireless networks

- N-Type Male to N-Type Female Connector.

- Optimal placement of your existing Wi-Fi Device permits you to maximize its wireless performance

- Flexible outer conductor allows the tightest bend radius available for any cable of similar size and performance

- Provides flexible Low-loss communication for wireless antenna

- 50dB RF Shielding is 10 dB greater than typical single shielded coax (40 dB).

- Multi-ply bonded outer foil conductor is rated conservatively at > 90 dB.

- Weatherproof cable design for outdoors exposure with best materials for UV resistance

- Polyethylene jacketed cable designed for outdoor use

- Easy and quick deployment into a WLAN environment

Specifications

| Construction | Electrical |
| --- | --- |
| Inner Conductor (BCCAI) | 0.108 in. (2.74 mm) | Cut-off Frequency | 16.2 GHz |
| Dielectric (Foam PE) | 0.285 in. (7.24 mm) | Velocity of Propagation | 85% |
| Outer Conductor (Aluminum Tape) | 0.291 in. (7.39 mm) | Dielectric Constant | 1.38 |
| Over Braid (Tinned Copper ) | 0.320 in. (8.13 mm) | Time Delay | 1.20 nS/ft (3.92 nS/m) |
| Jacket (PE) | 0.405 in. (10.29mm) | Impedance | 50 ohms |
| Mechanical | Capacitance | 23.9 pF/ft (78.4 pF/m) |
| Bend Radius: Installation | 1.0 in. (25.4mm) | Inductance | 0.060 uH/ft (0.20 uH/m) |
| Bend Radius: Repeated | 4.0 in. (101.6 mm) | Shielding Effectiveness | > 90 dB |
| Bending Moment | 0.5 ft-lb (0.68 N-m) | DC Resistance Inner Conductor Outer Conductor | 1.39 ohms/1000ft (4.6 ohms/km) 1.65 ohms/1000ft (5.4 ohms/km) |
| Weight | 0.068 lb/ft (0.10 kg/m) |  |  |
| Tensile Strength | 160 lb (72.6 kg) |  |  |
| Flat Plate Crush | 40 lb/in. (0.71 kg/mm) |  |  |
| Environment |  |  |
| Temperature | Operating: -40( C ~ 85(C (-40(F~185(F) Storage: -70( C ~ 85(C (-94(F~185(F) | Voltage Withstand | 2500 Volts DC |
|  |  | Jacket Spark | 8000 Volts RMS |
|  |  | Peak Power | 16 kW |

Package Contents							Related Product

- TEW-L406 / TEW-L408						- TEW-AO08O/TEW-AO10O

-	Weatherproof Tape 						- TEW-ASAK

- 	User’s Guide							- TEW-L202/TEW-L208

To order please call: 888-326-6061 • Sales: sales@trendnet.com

Support: support@trendnet.com • Tech Support Hotline: 1-888-777-1550

Official Site: www.trendnet.com

# Text boxes

N-Type Female
Connector

LMR400 N-Type Male to N-Type Female Cable

The LMR400 N-Type Male to N-Type Female cable extends your wireless Antenna up to 6 or 12 meters to provide optimal placement for your antenna outdoors. Connect business networks from building to building wirelessly or provide wireless Internet access for hot spot applications!  This cable makes wireless communication possible by providing low loss communication between your access point and antenna.

TEW-L406/TEW-L412

Antenna Cable Solution

N-Type Male
 Connector

Interface