Specifications

| Frequency range: | 2.4GHz ~ 2.5GHz |
| --- | --- |
| Gain: | 24 dBi |
| VSWR: | 1.5 : 1 Max |
| Polarization: | Linear, Vertical |
| HFBW Vertical | 14 o |
| HFBW Horizontal | 10 o |
| Front to Back Ratio: | 30dB |
| Up/Down tilt: | 60 o |
| Power Handling: | Max. 100 W (cw) |
| Impedance: | 50 Ohms |
| Connector Lead Cable: | RG-58/u, 30 cm (12 inches) |
| Connector Type: | N-Type Female |
| Survival Wind Speed: | 216 Km/hr (134 Miles/hr) |
| Temperature: | -40 oC ~ 80 oC (-40 oF ~ 176 oF) |
| Humidity: | 100% @ 25 oC (77 oF) |
| Lightning Protection: | DC Ground |
| Antenna Type: | Directional, Grid type |
| Mount Style: | Pole end mounting. Pole diameter 50mm (2 inches) max. |
| Weight: | 3.5 Kg (7.7 lb) |
| Dimensions (WxHxD): (Final product) | 90 x 60 x 50 mm (35.4 x 23.5 x 19.5 inches) |
| Warranty: | 3 Years |

To order please call: 888-326-6061

20675 Manhattan Place • Torrance, CA 90501 • (310) 891-1100 • Fax: (310) 891-1111

sales@trendnet.com • techsupport@trendnet.com

# Text boxes

## TEW-OA24D (v2.0R)

PRODUCT

INFORMATION

TEW-OA24D 24dBi Outdoor Directional Antenna

TEW-OA24D 24dBi High Gain Outdoor Reflector Grid Antenna provides extended coverage range for your existing 802.11b or 802.11g Wireless Local Area Network (WLAN). TEW-OA24D comes with female N-type antenna connector; with optional conversion cable (male N-type to female Reverse SMA). TEW-OA24D is weatherproofed; you can mount it outdoor on the wall or on a pole. The antenna also has a tilted bracket for antenna alignment. Expand the power of your wireless product with TRENDnet's TEW-OA24D.

Pattern

NOTE: For optimal results in extending your wireless range with wireless antenna installations, we recommended that you consult a professional installer for site survey, safety precautions, and proper installation.