Features

- Wi-Fi Compliant with IEEE 802.11b/g devices

- Compliant with USB 2.0 High-Speed Printing

- One RJ-45 10/100Mbps Auto-MDIX Fast Ethernet Port

- Supports WEP & WPA-PSK encryption

- Compliant with Windows 98SE/2000/XP/2003 Server and more

- LPR printing for Windows

- IPP printing for Windows 2000/XP

- Printing over Email and FTP

- Supports most Windows Graphical Devices Interface (GDI) printers

- Second HTTP port for remote Web configuration and IPP printing

- Supports SNMP v1.0 and MIB II (RFC-1213)

- Supports Macintosh Rendezvous Zero Configuration

- Windows-Based Program (PS Utility)

- Web-Based (HTTP) Configuration

- Built-in flash memory for easy firmware upgrade

- 3-Year Warranty

*Mac Systems are only compatible with Post-Script printers

Specifications

| Hardware |
| --- |
| Standards | Wired: IEEE 802.3 10Base-T, IEEE 802.3u 100Base-TX Wireless IEEE 802.11b/g |
| Printer Interface | USB 2.0, 1.1 Compliant USB Type A Port |
| LAN Port | 10/100Mbps Auto-Negotiation UTP/STP RJ-45 Port |
| CPU/ SDRAM / Flash ROM | RDC 2886 / 8Mbyte/ 2Mbye |
| LED | Power, Link/Act, WLAN, USB |
| Transport Protocol | TCP/IP, SMB, NetBEUI, AppleTalk |
| TCP/IP Protocol Supported | BOOTP, SNMP, Telnet, TFTP, FTP, LPD, RARP, DHCP, IPP |
| OS Support | Windows 95/98(SE)/ME/NT/2000/XP/2003 Server Netware 5.x NDPS LPR Remote Printing (TCP/IP), HP-UX Unix, Sun OS, Solaris, SCO Unix, AIX, Unixware, Linux & Mac OS (AppleTalk) |
| Management | Windows Utility or Web-Browser Configuration |
| Power | 5V DC 2.5A External Power Adapter |
| Dimensions | 115 x 85 x 38mm (4.5 x 3.4 x 1.5in.) |
| Weight | 160g (5.6oz.) |
| Temperature | Operating: 0(C~50(C (32(F~122(F) Storage: -25(C~55(C (-13(F~131(F) |
| Humidity | 10%~90% (non-condensing) |
| Certification | CE, FCC |
| Wireless |
| Frequency | 2.4 ~ 2.4835 GHz (Industrial Scientific Medical Band) |
| Encryption | 64/128-bit WEP (HEX/ASCII), WPA-PSK(TKIP) |
| Antenna | 2dBi Detachable Reverse-SMA (Female) Diversity Antenna |
| Data Rate (Auto Fallback) | 802.11g: 54Mbps, 48Mbps, 36Mbps, 24Mbps, 18Mbps, 12Mbps, 9Mbps and 6Mbps 802.11b: 11Mbps, 5.5Mbps, 2Mbps and 1Mbps |

Package Contents							Related Products

- TEW-P1UG								- TEW-432BRP

- Multi-Language Quick Installation Guide				- TEW-421PC

- Utility & User’s Guide CD-ROM					- TEW-423PI

- Power Adapter (5V DC, 2.5A)

To order please call: 888-326-6061; Sales: sales@trendnet.com

Support: support@trendnet.com; Tech Support Hotline: 866-845-3673

Official Site: www.trendnet.com

# Text boxes

Network Solution for TEW-P1UG

54Mbps 802.11g Wireless 1-Port USB 2.0 Print Server

TEW-P1UG is a print server that transforms virtually any stand-alone USB network printer into a shared network printer. The TEW-P1UG provides IEEE 802.11g 54Mbps wireless interface for integrating into existing wireless network. The TEW-P1UG is designed for printers equipped with USB 2.0 compliant printer port and it is an ideal network solution to convert conventional USB printer into a shared resource on the network.

TEW-P1UG (Version B.1R)

Interface