Features

- Detects 2.4 GHz wireless signals generated from 802.11b/g Wi-Fi device, cordless phone, microwave oven and wireless hidden camera

- Helps Network Administrators survey the environment and locate the interference easily

- Verifies Wi-Fi signal strength, allowing Better Configuration

- Indicates signal strength with Diagnostic LEDS

- Displays signal source with Diagnostic LEDS

- Operates at 0.5 seconds for super fast signal detection

- Offers Automatic-Alert, Automatic-Silent, and Manual Scan modes

- Scans for 30 minutes and automatically turns off in Automatic scan mode

- Uses low battery LED to preclude incorrect reading

- Supports Range of up to 20~45 meters indoor, 60~90 meters outdoor

(Depends on the environment)

- 2-year warranty

Specifications

| Hardware |
| --- |
| Compatibility | 2400 – 2480 MHz , IEEE 802.11b/g |
| LED Indicators | Signal Strength, Signal Source, Power, Battery |
| Antenna Direction | 3 dBi Outward Directional from back of the detector |
| Power Consumption | Signal Detected – 28 mA/sec Mute Signal Detected – 20 mA/sec Scanning – 10 mA/sec |
| Receiver Sensitivity | Top LED: -40 dBm Second LED : -45 dBm Third LED : -50 dBm Bottom LED: -55 dBm |
| Operation Voltage | 2.6V-3.3V |
| Data Range | Indoor: 20~45m (60~150ft) Ourdoor: 60~90m (200~300ft) |
| Battery (included) | 2 x Size AAA, 1.5 Volt battery (Non-Rechargeable battery only) |
| Battery Life | Signal Detected – 10 hours Mute Signal Detected – 30 hours Stand by – 1 year |
| Temperature | Operation: 0(C~43(C (32(F~110 (F) Storage: -12(C~48(C (10(F~120 (F) |
| Humidity | 10%- 90% (non-condensing) |
| Dimensions (L x W x H) | 59mm x 15mm x 102mm (2.3 x 0.6 x 4.0 inches) |
| Weight | 65 g (0.14 lb) included batteries |
| Certification | CE |

TOP REASONS THE TEW-T1 IS A LASTING TREND

| Integration Friendly | No software required. |
| --- | --- |
| Economical | Locate Wi-Fi signal quickly, saving time and labor. |
| Flexible | Easy to read LEDs, indicating signal sources and strength |
| Performance | Detecting Range up to 90m/300ft away |

* If the Detector detects multiple devices, then the Detector displays the signal strength of the device with

the strongest signal.  Detection of multiple devices also means possible interference.

Package Contents	Related Product

- TEW-T1	- TEW-410APBplus

- Multi-Language User’s Guide	- TEW-IA04O

- 2 x 1.5V AAA Battery	- TEW-IA06D

To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

### Sales: sales@trendware.com • Support: techsupport@trendware.com

Tech Support Hot Line: 1-310-626-6252  Official Site: www.TRENDNET.com

# Text boxes

Wi-Fi Environment

TEW-T1

2.4 GHz Wi-Fi Detector

TRENDnet’s TEW-T1 effortlessly reveals Wi-Fi hot spots and conveniently locates optimum wireless network access with visual feedback. The TEW-T1 intelligently distinguishes other radio frequency transmissions to avoid possible signal interference.

Side View