#### Features

- Compliant with IEEE 802.3ab 1000Base-T and IEEE 802.3z 1000Base-LX Standards

- Provides Dip Switch for Fiber (Auto/Manual), LLR (Enable/Disable)

- Support LLCF (Link Loss Carry Forward, Link Pass Through)

- Supports LLR (Link Loss Return) for FX Port

- Supports Full-Duplex and Auto-Negotiation Mode for Fiber Port

- Single-Strand Fiber Optic, Hot Pluggable & Wall-Mountable

- Optional 19” System Chassis (TFC-1600) holds up to 16 Media Converter

- 5-Year Warranty

#### Specifications (MMF: Single-Mode Fiber)

| Model Name | Wavelength | Pout | Sensitivity | Power |
| --- | --- | --- | --- | --- |
| TFC-1000S10D3 | TX: 1310nm; RX: 1550nm | -9dBm | -21dB | 12dBm |
| TFC-1000S10D5 | TX: 1550nm; RX: 1310nm | -9dBm | -21dB | 12dBm |

| Hardware |
| --- |
| Standard | IEEE 802.3ab 1000Base-T IEEE 802.3z 1000Base-LX |
| Network Media | 1000Base-TX: UTP Cat. 5, EIA/TIA-568 100-ohm STP, up to 100meters 100Base-LX: 10/125μm Single-Fiber Optic Cable, up to 10km |
| Protocol | CSMA/CD |
| Ports | 1 x 1000ase-T RJ-45 Port 1 x 1000Base-LX Single-Fiber Bi-Directional Port SC Connector |
| Dip Switch | TX: Duplex Mode, Auto Negotiation or Manual, Speed, LLCF (enable/disable) FX: Duplex Mode, LLR (enable/disable), LLCF |
| Transfer Rate | 1000Base-T : 2000Mbps (Full Duplex) |
| Diagnostic LED | Per Unit : Power Per Port : Link/Activity |
| Power Adapter | 7.5V DC, 1.5A External Power Adapter |
| Power Consumption | 5.5 watts (max) |
| Dimensions | 120 x 88 x 25mm (4.7 x 3.46 x 0.98 inches) |
| Weight | 354g (12.5oz) |
| Temperature | Operating : 0( ~ 40( C (32( ~ 104( F) Storage : -25( ~ 70( C (-13( ~ 158( F) |
| Humidity | 5% ~ 90% RH |
| Safty Emissions | FCC,CE |

To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

Sales: sales@trendnet.com • Support: techsupport@trendnet.com

Tech Support Hotline: (888)777-1550

www.trendnet.com

# Text boxes

1000Mbps TX to 1000Base-FX Single-Mode Fiber Converter

The Single-strand fiber products use optics that transmit and receive on two different wavelengths; you must deploy single-strand fiber products in pairs, or connect two compatible TFC-1000S10 series single-strand fiber products. For example, connect TFC-1000S10D3 (which has 1310 transmit and 1550 receive) to TFC-1000S10D5 (which has 1550 transmit and 1310 receive). The two connected products must also have the same speed, and distance capabilities (i.e. both support single-mode, 10km distance).

TFC-1000S10D3/D5