#### Features

- Compliant with IEEE 802.3ab 1000Base-T, 802.3z 1000Base-LX

- One 1000Base-T Auto-MDIX RJ-45 port

- One 1000Base-LX Single-mode SC-type Fiber port

- Supports LLCF (Link Loss Carry Forward)

- Provides Dip switches to enable LLCF function in both TX and Fiber port

- Diagnostic LEDs

- Plug & Play, Hot Swappable

- Optional 19” Fiber Converter Chassis (TFC-1000) holds up to 10 Fiber Converters

- 5-Year Warranty

#### Specifications

|  | Media | Wavelength | Power Output (dBm) | Sensitivity (dB) | Power Budget (dBm) | Distance |
| --- | --- | --- | --- | --- | --- | --- |
| TFC-2000S20 | SMF (9/125 µm) | 1310nm (1270 nm~1355nm) | -8 | -23 | 15 | 20km |
| TFC-2000S50 | SMF (9/125 µm) | 1550nm (1520nm ~ 1580nm) | -4 | -23 | 19 | 50km |

| Hardware |
| --- |
| Standard | IEEE 802.3ab1000Base-T IEEE 802.3z 1000Base-LX |
| Network Media | 1000Base-T: Cat. 5e, 6 1000Base-LX: 9/125μm Single-Mode Duplex SC-Type Fiber Cable |
| Minimum Cable Length | 50 Meters |
| Protocol | CSMA/CD |
| Frame Packet Size | 64 to 1536 Bytes |
| Ports | 1 x 1000Base-T RJ-45 Port 1 x 1000Base-LX: Single-Mode SC-Type Fiber Port |
| Dip Switch | Dip Switch 1: ON: TX Port LLCF Enable OFF: TX Port LLCF Disable Dip Switch 2: ON: Fiber Port LLCF Enable OFF: Fiber Port LLCF Disable * After changing the DIP Switch settings, power cycle the Fiber Converter. |
| Transfer Rate | 1000Mbps (Half/Full Duplex) |
| Diagnostic LED | Per Device: Power Per Port (TX): 1000Mbps, Link/Activity, Full Duplex/Collision (FX): Link/Activity, Full Duplex/Collision |
| Power Adapter | 9V DC, 700mA External Power Adapter |
| Power Consumption | 3.6 Watts (max) |
| Dimensions | 85 x 125 x 25mm (3.35 x 4.92 x 0.98in.) |
| Weight | 300g (10.6oz.) |
| Temperature | Operating : 0( C ~ 45( C (32( F ~ 113( F) Storage : -40( C ~ 70( C (-40(F ~ 158( F) |
| Humidity | 5% ~ 90% RH |
| Certification | CE, FCC |

To order please call: 888-326-6061 • Sales: sales@trendnet.com
Support: support@trendnet.com • Tech Support Hotline: (866)845-3673

www.trendnet.com

# Text boxes

TFC-2000S50 (v1.0R)

_

1000Base-T to 1000Base-LX 
SC-Type Single-Mode Fiber Converter

This Fiber Converter with SC-Type connector transforms 1000Base-T UTP/STP media to 1000Base-LX single-mode. The 1000Base-T port supports auto-MDIX.   Designed to connect up to 50KM, the converters are the perfect Gigabit, single-mode solution.