#### Features

- Compliant with IEEE 802.3 10Base-T and IEEE 802.3u 100Base-TX, 100Base-FX standards

- One 10/100Base-TX Auto-Negotiation/Auto-MDIX RJ-45 port

- One 100Base-FX Dual-Wavelength Single-Mode Single-Strand SC-type Fiber port

- Supports LLCF (Link Loss Carry Forward)

- Provides Dip switch to set: UTP (Auto Negotiation/Full Duplex), Fiber (Hall Duplex/Full Duplex) , LLCF (Enable/Disable), Mode (Pure Converter Mode/ Switch Converter Mode)

- 802.3x flow control for 10/100Base-TX port

- Plug & Play, Hot Pluggable

- Diagnostic LEDs

- Optional 19” Fiber Converter Chassis (TFC-1000) holds up to 10 Fiber Converters

- 5-Year Warranty

#### Specifications

| Model Name | Media | Wavelength | Power Output (dBm) | Sensitivity (dB) | Power Budget (dBm) | Distance |
| --- | --- | --- | --- | --- | --- | --- |
| TFC-210S20D3 | WDM (Single Mode) | TX:1310nm (1260nm~1360nm) RX:1550nm (1480nm~1600nm) | -14 | -31 | 17 | 20KM |
| TFC-210S20D5 | WDM (Single Mode) | TX:1550nm (1480nm~1580nm) RX:1310nm (1260nm~1360nm) | -14 | -31 | 17 | 20KM |

- The Single-Strand WDM Single-Mode Fiber Converter TFC-210S20D3 must be paired with TFC-210S20D5.

| Hardware |
| --- |
| Standard | IEEE 802.3 10Base-T IEEE 802.3u 100Base-TX, 100Base-FX |
| Network Media | 10Base-T: UTP/STP Cat. 3, 4, 5, EIA/TIA-568 100-ohm 100Base-TX: UTP/STP Cat. 5, EIA/TIA-568 100-ohm 100Base-FX: 9/125um Single-Strand Fiber Optic Cable, up to 20km |
| Minimum Cable Length | 50 Meters |
| Protocol | CSMA/CD |
| Frame Packet Size | 64 to 1600 Bytes |
| Ports | 1 x 10/100Base-TX: RJ-45 Port 1 x 100Base-FX : Single-Mode Bi-Directional SC-Type Fiber Port |
| Dip Switch | Dip Switch 1: ON: TX Port Fully Duplex OFF: TX Port Auto- Negotiation Dip Switch 2: ON: FX Port Half Duplex OFF: FX Port Full Duplex Dip Switch 3: ON: LLCF Enable OFF: LLCF Disable Dip Switch 4: ON: Pure Converter Mode OFF: Switch Converter Mode * After changing the DIP Switch settings, power cycle the Fiber Converter |
| Transfer Rate | 100Mbps (Half/Full Duplex) |
| Diagnostic LED | Per Device: Power Per Port (TX): 100Mbps, Link/Activity, Full Duplex/Collision (FX): Link/Activity, Full Duplex/Collision |
| Power Adapter | 9V DC, 700mA External Power Adapter |
| Power Consumption | 3.1 Watts (max) |
| Dimensions | 85 x 125 x 25mm (3.35 x 4.92 x 0.98in.) |
| Weight | 300g (10.6oz.) |
| Temperature | Operating : 0( C ~ 45( C (32( F ~ 113( F) Storage : -40( C ~ 70( C (-40(F ~ 158( F) |
| Humidity | 5% ~ 90% RH |
| Certification | CE, FCC |

# Text boxes

TFC-210S20D3 (v1.0R)

_

10/100Mbps-TX to 100Base-FX Dual-Wavelength 
Single-Mode Fiber Converter

TFC-210S20D3 Bi-Directional Single-Fiber Media Converter transforms 10/100Mbps-TX UTP/STP media to 100Base-FX media and vice versa. The 10/100Mbps-TX Port Auto-Negotiating 10 or 100Mbps connection speed with Auto-MDIX media type, the fiber supports single-mode SC type connection. This converter will give your Switch/Hub the ability to interface with fiber connection over a distance up to 20 km.