#### FEATURES

- IEEE 802.3u 100Base-FX standard compliant

- Auto-Negotiation for half-duplex/full-duplex

- Coverts single channel 100Mbps Multi-mode SC fiber to Single-mode SC fiber

- Status LED indicators for Power and Link

- Extends single-mode fiber optic cable distance up to 75Km (depends on the model)

- Wall-Mountable

- Optional 19” system chassis holds up to 16 TFC series Media Converters

- 5-year Warranty

#### TREND SPEC’S

Standards:		IEEE 802.3u 100Base-FX

Ports:			2 x 100Base-FX

FX port Media Types:	Port 1:Multi-mode SC, Port 2: Single-mode SC

Network Media:	100Base-FX: 50/125μm or 62.5/125μm multi-mode fiber optic cable, up to

2 Km. 9/125 μm or 10/125μm single-mode fiber optic cable, up to 75 Km (depends on the model)

Protocol:			CSMA/CD

Data Transfer Rate:	100Mbps (Half-Duplex), 200Mbps (Full-Duplex)

Diagnostic LEDs:	Power, Link

Power Adapter:	7.5VDC, 1.5A (7.2 watts max.)

Dimensions:		120 x 88 x 25 mm (W x D x H)

Weight:			Appro. 305 g. (10.8 Oz.)

Temperature:		Operating: 0( ~ 40( C (32( ~ 104( F), Storage: -25( ~ 70( C (-13( ~ 158( F)

Humidity:		Operating: 10% ~ 90%, Storage: 5% ~ 90% (non-condensing)

Certifications:		FCC, CE, VCCI

TFC-15MS100 	100Base-FX Multi-mode to Single-mode 15 Km Fiber with SC Connector		TFC-40MS100	100Base-FX Multi-mode to Single-mode 40 Km Fiber with SC Connector

TFC-75MS100	100Base-FX Multi-mode to Single-mode 75 Km Fiber with SC Connector

TFC-1600	16-slot EIA-19” (2 Unit-Height) Chassis for TFC series Media Converters

TFC-1600MM	Media Converter Chassis Management Module

TFC-1600RP	Media Converter Chassis Redundant Power Supply

To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

## Sales: sales@trendware.com • Support: techsupport@trendware.com

# Text boxes

Product Information

### TFC-MS100

Fiber Media Converter

TRENDnet’s TFC-MS100 series Fiber Media Converter transforms 100Base-FX Multi-mode fiber media to 100Base-FX single-mode fiber and vice versa. Both 100Base-FX ports auto-negotiate half-/full-duplex connection and Port 1 supports multi-mode SC connector and Port 2 supports single-mode SC connector. This converter will give your Switch/Hub the ability to interface with fiber connections over a distance up to 75 Km. With the optional 16-slot EIA-19” Rack-Mount Chassis and Management Module, the TFC series converters are the perfect solutions for various fiber media conversions for your network.