FEATURES

- PCMCIA 2.1/JEIDA 4.1 compliant

- High performance 16C550A compatible UART

- Hayes 'AT'-command compatible

- Advanced Plug and Play technology to run with Windows 95/98/ME/2000/NT/XP and Linux

- Data and fax software for Windows included

- Automatic sleep mode to extend PC battery life

- RJ-11 cable (included) with internal DAA for direct connection to the telephone wall socket

- High speed 56Kbps data and 14.4Kbps fax communication

- Industry standard protocol for data compression and error correction

- 5 Year Warranty

TREND SPEC’S

Operating Protocol:	V.90 (56,000bps); K56flex (56,000 bps); V.34bis (33,600 bps); V.34 (28,800 to 2,400 bps); V32bis (14,400/12,000/9,600/7,200 bps); V.32 (9,600/4,800 bps); V.22bis (2,400 bps); V.23 (1,200 TX/75 RX bps); V.22/Bell 212A (1,200 bps); V.21/Bell 103 (300bps)

Error Control Protocol:		V.42 and MNP Class 2 to 4

Data Compression Protocol:	V.42bis and MNP Class 5

Fax Compatibility:	EIA Class 1 fax commands; Group 3 send and receive; ITU-T V.17 up to 14,400 bps; ITU-T V.29 up to 9,600 bps; ITU-T V.27ter up to 4,800 bps; ITU-T V.21 Channel 2 up to 300 bps

Dialing Capability:		DTMF tone; Rotary pulse

Operating Modes: 	Asynchronous full duplex; Manual/automatic answer

Flow Control: 	Hardware CTS/RTS; Software XON/XOFF

Receive Sensitivity:	 -40dBm

Transmit Level: 	Permissive -11 (±) 1dBm

Line Interface: 	RJ-11, 2-wire dial-up

Diagnostics:	Power-up self-test; Local analog loopback test; Local analog loopback with self-test; Local digital loopback test; Remote digital loopback test; Remote digital loopback with self-test

Software Control Interface: 	Hayes compatible AT command set

Call Progress Monitoring: 	Dial Tone, Busy Tone, Ring-back Detection

Typical Power Consumption: 	Operation: 640mW; Sleep mode: 80mW

Dimension: 			Comply with PCMCIA Type II; 85.6mm x 54mm x 5mm (3.37" x 2.128" x 0.197")

Weight: 				8.5g (0.3Oz.)

Certification:			CE, FCC

TOP REASONS THE TFM-560E IS A LASTING TREND

User Friendly:	Just plug the card into your workstation and it’s ready to go!

Flexibility:	A single card supports both V.90 and K56Flex data/fax protocols.

Compatibility:	The TFM-560E card supports a variety of software.

Speed:	Up to 56Kbps download speed and 14.4Kbps fax communication

TFM-560E	PCMCIA 56K (V.90) High Speed Fax Modem (Agere Chipset)

TFM-560R	PCMCIA 56K (V.90) High Speed Fax Modem with Xpress Port (Agere Chipset)

TEM100-56R	PCMCIA 10/100Mbps Fast Ethernet + 56Kbps Fax Modem Adapter with Xpress Port

To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

Sales: sales@trendware.com • Support: Techsupport@trendware.com 		SS111802

# Text boxes

56Kbps (V.90) High Speed PCMCIA

Fax Modem

Experience quick dial-up access with TRENDnet’s TFM-560E high speed PCMCIA fax modem. The TFM-560E is a V.90/K56Flex ultra fast 56Kbps data/fax modem that provides users with high data communication rates, reliable error-free transmissions, and widespread interoperability with other users. This modem is Bell/ ITU compliant and Hayes AT command compatible; therefore it can be used with most popular software programs (Free communication software included). The TFM-560E also supports Group 3 fax send-and-receive functions.  This fax modem complies with the PCMCIA Type II slot standard and is ideal for on-the-go Notebook users

TFM-560E

PCMCIA Fax/Modem Applications

PRODUCT

INFORMATION