FEATURES

- V.90 56Kbps data download

- Supports V.17, V.29, and V.27ter Group 3 fax protocol

- Supports auto diagnostic

- Group 3 fax protocol / RS-232 interface

- Automatic detection for speed

- Voice encoding and decoding/TAM functions

- Telephony answering machine with full-duplex speakerphone

- High speed 56Kbps data and 14.4Kbps fax communication

- Industry standard protocol for data compression and error correction

- Free Communication Software

- 5-year warranty

TREND SPEC’S

Standards:			V.34+, V.32bis, V.23, V.22bis, V.22, V.21 ITU-T Data Transmit

Fax Protocol:			V.17, V.29, and V.27ter Group 3 fax protocol

Fax Command Set: 		Class 1 (TIA-578)

Error Control:			V.42LAP-M MNP Class 2-4

Data Compression:		V.42bis (4:1) MNP Class 5 (2:1)

Flow Control:	Hardware RTS/CTS, Software XON/XOFF

Software Control:		Industry Standard AT command set, Hayes compatible

Diagnostics:	Automatic power-on, self-test, local analog loopback, local digital loopback, and remote digital loopback

Voice Functions:	Voice encoding/decoding, telephony answering machine, and full-duplex speakerphone

Power Supply:			9V AC, 1Amp.

Power Consumption:	500mW

Dimensions:			165 x 138 x 35 mm

Weight:			330 g.

Temperature: 			Operating: 0° ~ 40° C.  Storage: -20° ~ 60° C

Humidity:			10 ~ 90%

Certifications:			UL, FCC, CE

### TOP REASONS THE TFM-560X IS A LASTING TREND

User Friendly: 		Easy installation and startup can be accomplished!

Speed:		 	The TFM-560 is capable of V.90 56,000bps download speed.

Versatility:	 	Provides fax capability and voice communication.

Affordability: 	TRENDnet’s TFM-560X completes voice, data, and fax set of standards.

TFM-560X	External 56Kbps (V.90) High Speed Internet Voice/Fax Modem

TFM-560P	PCMCIA 56Kbps (V.90) High Speed Fax Modem (Lucent Chipset)

TFM-560E	PCMCIA 56Kbps (V.90) High Speed Fax Modem (Cirrus Logic Chipset)

To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

Sales: sales@trendware.com • Support: techsupport@trendware.com

# Text boxes

TFM-560X

TFM-560X

### External 56K (V.90) High Speed Voice/Fax Modem

TRENDnet’s External 56K (V.90) High Speed Voice/Fax Modem

TRENDnet's TFM-560X is the latest in communication innovation. The TFM-560X is V.90 ultra fast 56Kbps voice/fax modem that provides users with the highest possible data communication rates, reliable error-free transmissions, and widespread interoperability with other users. The TFM-560X also supports Group 3 fax send-and-receive functions. Free communication software and serial cable are included with the TFM-560X for quick and easy startup. TRENDnet’s TFM-560X is also compatible with all communication software and capable of utilizing the Hayes 'AT'-command set.

## PRODUCT

INFORMATION