Features

- ITU-T V.92/V.90 Auto Detection and Auto Rate Adaptive

- High Speed 56kbps Data Transfer Rate with Maximum Degree of Interoperability

- V.44 and V.92 Features Support Quick Connect, PCM Upstream and Modem On Hold

- Robust Hardware Component Supports Software-Only Upgrades

- Supports High Speed Analog Data and High Speed Fax

- Fax Transfer Rate up to 14.4 kbps with ITU-T T.31 Fax Standard

- Built-in RS-232 Serial Interface for Connection

- Compatible with Windows 95/98/ME/NT4/2000/XP/2003 Operating Systems

- Supports TAM (Telephone Answering Machine) for Remote Message Retrieval

- Free Communication Software

- 5-Year Warranty

Specifications

| Hardware |
| --- |
| Standards (Compatible with ITU and Bell Standards) | V.92 56 Kbps ITU standard V.90 56 Kbps ITU standard V.34 33.6 Kbps ITU standard V.32bis, V.32, V.22bis, V.23, V.21, Bell 212A, Bell 103 |
| Error Correction | V.42, LAP-M & MNP 2-4 |
| Data Compression | V.44, V.42bis & MNP5 |
| Fax | ITU-T T.31 Fax Send and Receive V.17, V.29, V.27ter, and V.21 ch2 EIA/TIA-578 Fax Class1 Command |
| PC Telephony | International Telephony Support ITU-T V.250 AT Command Set |
| Supported Features | Data/Fax Call Discrimination Call Progress |
| Supported OS | Windows 95/98(SE)/ME/NT4/2000/XP/2003 Server, Mac OS and Linux |
| Interface | PC: RS-232 PSTN: RJ11 (Telephone Line) |
| Power | 9V AC, 1000mA External Power Adapter |
| Power Consumption | 995mW (max) |
| Dimension (Lx W x H) | 153 x 109 x 29mm (6 x 4.3 x 1.1 inches ) |
| Weight | 200g (7 oz.) |
| Temperature | Operating : 0( ~ 50( C (32( ~ 122( F) Storage : -20( ~ 60( C (-4( ~ 140( F) |
| Humidity | 10 ~ 90% (Non-Condensing) |
| Certification | FCC, CE |

Package Contents				Related Products

- TFM-560X					- TFM-PCIV92A

- Quick Installation Guide			- TFM-PCIV92I

- Software & User’s Guide CD-ROM 		- TFM-560U

- Power Adapter (9VAC, 1000mA)

- 1 x RJ11 Telephone Cable

- 1 x RS-232 Serial Cable

To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

Sales: sales@trendware.com • Support: techsupport@trendware.com

Tech Support Hotline: 1-310-626-6252

Official Site: www.TRENDnet.com

# Text boxes

TFM-560X (version Y0)

TFM-560X

### V.92 56K External Data/Voice/Fax Hardware Modem

V.92 56K External Data/Voice/Fax Modem

TRENDnet's TFM-560X is the latest in communication innovation. The TFM-560X is V.92 fast 56Kbps voice/fax modem that provides users with the highest possible data communication rates, reliable error-free transmissions, and widespread interoperability with other users. The TFM-560X also supports Group 3 fax send-and-receive functions. Free communication software and serial cable are included with the TFM-560X for quick and easy startup. TRENDnet’s TFM-560X is also compatible with virtually all communication software and capable of utilizing the AT command set.

On/Off Switch

Power

Serial Port

RJ11 Ports

Diagnostic LEDs