Features

- Compliant with USB 2.0, USB 1.1 and FireWire IEEE 1394 Specifications

- Supports USB High-Speed Transfer Rate up to 480 Mbps

- Supports IEEE 1394 Transfer Rate up to 400Mbps

- Supports USB Over-Current Detection and Individual/Gang Power Control

- High Speed Detection Indicator Output

- Supports Multiple tiers with up to 127 USB Devices and up to 63 FireWire Devices

- Compliant with Windows 98SE/ME/2000/XP

- Supports Bus-Power or Cable-Power with Power Adapter

- Compatible with USB 2.0/1.1 and FireWire enabled PCs

- Supports Plug & Play and Easy Installation

- 2-Year Warranty

Specifications					      	Solution for TFU-430

| Hardware |
| --- |
| Interface | USB 2.0 and FireWire |
| Standards | USB 2.0, 1.1 and FireWire IEEE 1394 |
| Port | 1 x USB 2.0 Type B Port (Uplink) 4 x USB 2.0 Type A Ports 3 x FireWire Ports |
| Driver Compliant | Windows 98SE/ME/2000/XP Mac OS 8.6/9.x/10.x |
| LED | Power : USB & FireWire USB : Link Activity |
| Dimension (LxWxH) | 106.5 x 63 x 41.5mm (4.2 x 2.48 x 1.6 inches) |
| Weight | 145g ( 3.2lb) |
| Data Rate | USB: 1.5Mbps, 12Mbps, 480Mbps FireWire: 100Mbps, 200Mbps, 400Mbps |
| Power Adapter (Switching) | Input: 100~240V ~ 50/60Hz Output: 12V DC, 2.5A |
| Power Consumption | 500mA (max) |
| Operating Temperature | 0( ~ 40( C (32( ~ 104( F) |
| Storage Temperature | -10( ~ 45( C (14( ~ 113( F) |
| Humidity | 85% (Non-Condensing) |
| Certification | FCC, CE |

Package Contents	-     TFU-430				Related Products	- TMR-61U2

- Quick Installation Guide					- TU2-ET100

- 1 x FireWire Cable (1.8m/6ft.)					- TU2-ET200

-	1 x USB 2.0 Cable (1.8m/6ft.)

- Power Adapter

# Text boxes

TFU-430

7-Port USB2.0/FireWire Combo Hub

This 7-Port USB 2.0/FireWire Combo Hub provides four USB 2.0 ports and three IEEE 1394 FireWire ports to your USB/FireWire-Enabled Desktop or Laptop PC.

Front View

Back View