###### FEATURES

- Support Microsoft Intellimouse, Microsoft Intellimouse Explorer, Logitech NetMouse, Optical Mouse, Cordless Mouse and other Microsoft compatible mouse

- PS/2 Keyboard/Mouse emulation

- Supports DOS, Windows 3.x/95/98/ME/NT/2000/XP, Netware, Unix, Linux, and more

- Very high video quality – up to 1920 x 1440 resolution and 200Mhz bandwidth

- No software required – easy PC selection via Push Buttons and Hot-Key Operations

- Hot-Plug feature – add or remove PCs without powering off the KVM Switch or other PCs

- Auto-Scan Mode for monitoring PCs; with configurable scan interval from 5 ~ 99 seconds

- Keyboard status restored when switching between PC’s

- LED Display for easy status monitoring

- Beeping sound for port switching confirmation (could be disabled in auto-scan mode)

- EIA-19” rack-mountable (hardware included)

- 1-Year Warranty

###### TREND SPEC’S

Computer Port:		16 ports. Keyboard and Mouse: PS/2 type mini Din 6-pin (female),

VGA: HDDB 15-pin (female)

Console Port:		1 port. Keyboard and Mouse: PS/2 type mini Din 6-pin (female),

VGA HDDB 15-pin (female)

PC Selection:			Hot-Keys and Push Buttons

LED Segment:		Two LED indicators per port (PC Link (green) and PC Active (red))

Auto-Scan Interval:		5 ~ 99 seconds

Keyboard State:		Saved and restored

Video Bandwidth:		200MHz

Power Adapter:		External AC Power adapter, 12V DC, 1A

Dimensions:			406.0 x 163.5 x 85.0 mm (15.98 x 6.44 x 3.35 inches)

Weight:			2.65 Kg. (5.85 lbs)

Operating Temp.:		0( ~ 40( C (32( ~ 104( F)

Storage Temp.:		-20( ~ 60( C (-4( ~ 140( F)

Operating Humidity:		0% ~ 80% (non-condensing)

Emissions:			FCC, CE

TOP REASONS THE TK-1601R IS A LASTING TREND

Integration Friendly:	Does not require driver/software for the installation and operation. Switching between PCs with the Push Buttons and Hot-Key operations.

Flexible:	Hot-Plug feature – add PCs or remove connected PCs without powering off the KVM Switch or the other PCs.

Cost Effective:	Manage multiple PCs with single keyboard, monitor, and mouse. Save on equipment cost, utility, and space.

Performance:	Support very High Video Quality up to 1920 x 1440 with 200Mhz bandwidth. Keyboard status is saved for each PC.

TK-1601R		16-Port Rack Mount KVM Switch

TK-200K		2-Port KVM Switch Kit

TK-205i		2-Port KVM Switch with Integrated Cables

TK-400K		4-Port KVM Switch Kit

TK-401R		4-Port Rack Mount KVM Switch

TK-801R		8-Port Rack Mount KVM Switch

TK-802R		8-Port Stackable Rack Mount KVM Switch (with OSD)

TK-C06		6-Feet KVM Cable (male-to-male)

TK-C10		10-Feet KVM Cable (male-to-male)

TK-C15		15-Feet KVM Cable (male-to-male)

##### To order please call: 888-326-6061

#### 3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

Sales: sales@trendware.com • Support: techsupport@trendnet.com 	09082003

# Text boxes

16-Port Rack Mount KVM Switch

TRENDnet TK-1601R 16-Port KVM Switch allows you to manage up to 16 PC’s with just one keyboard, monitor, and mouse.  Switches between multiple PCs with a simple press of a button! Eliminates the hassle of cable swapping, save money and space with the TK-1601R. This KVM Switch also comes with a rack-mount kit for mounting on standard EIA-19” equipment rack in the Server Room and Computer Lab. Rich in features such as Hot-Plug, Auto-Scan, and Hot-Key operations; TRENDnet TK-1601R is the perfect choice for managing multiple PCs.

TK-1601R

KVM Solutions for TK- 1601R

Product Information