Features

- 4-Port PS/2 Audio KVM Switch with Audio and Microphone switching

- PS/2 style keyboard and mouse control

- Simultaneous/Independent Switching of Audio-Microphone and PC channel

- Supports Microsoft IntelliMouse, IntelliMouse Explorer, Logitech NetMouse and more

- Additional advanced support for High-End Logitech Wired/Wireless/Optical Mice

- High Quality of up to 2048 x 1536 VGA Resolution

- Direct Channel Selection and Operation using Push Buttons or Hot-Key Commands

- Mouse Reset Hot-Key Support for non-PnP OS such as WinNT 4.0 and Linux

- Auto-Scan Mode for monitoring PCs and Beeping Sound for Switching Confirmation

- Supports DOC, Windows 95/98(SE)/ME/2000/XP, Linux and more

- Plug & Play and Hot-Pluggable

- EIA-19” (1U) Rack-Mountable (kit included)

- 2-Year Warranty

Specifications

| Hardware |
| --- |
| PC Port Connector | 4 x PS/2 Keyboard 6-pin Mini Din (Female) + Audio 4 x PS/2 Mouse 6-pin Mini Din (Female) + Microphone 4 x VGA HDB 15-pin (Female) |
| Console Ports Connector | 1 x PS/2 Keyboard 6-pin Mini Din (Female) 1 x PS/2 Mouse 6-pin Mini Din (Female) 1 x VGA HDB 15-pin (Female) 1 x 3.5mm Audio in/out jack 1 x 3.5mm Microphone in/out jack |
| Cable 4 sets of Audio KVM Cable (1.8m/6ft) | To KVM PS/2 Keyboard 6-pin Mini Din (Male) PS/2 Mouse 6-pin Mini Din (Male) VGA HDB 15-pin (Male) To PC PS/2 Keyboard 6-pin Mini Din (Male) PS/2 Mouse 6-pin Mini Din (Male) VGA HDB 15-pin (Male) Audio connector (Male) Microphone connector (Male) |
| PC Selection | Push Buttons or Hot-Key Commands |
| Auto Scan Intervals | 5~100 seconds (default 5 seconds) |
| Keyboard/Mouse Emulation | PS/2 |
| Display Resolution | 2048 x 1536 |
| Power | Bus-Powered, Optional Adapter : 9V DC, 500mA (not included) |
| Dimensions | 255 x 117.5 x 45mm (10 x 4.6 x 1.8 inches) |
| Weight | 1000 g (35.2 oz.) |
| Temperature | Operating: 0( ~ 40(C (32( ~104( F); Storage: -20( ~ 60(C (-4( ~ 140( F) |
| Humidity | 0%~90% RH, Non-Condensing |
| Certifications | FCC, CE |

TOP REASONS THE TK-403KR IS A LASTING TREND

| Integration Friendly | Does not require driver/software for the installation and operation. Switch between PCs with the push button or Hot-Key operation. |
| --- | --- |
| Flexible | Hot-Plug feature, add PCs or remove connected PCs without powering off the KVM switch or the other PCs. |
| Cost Effective | Manage two PCs with single keyboard, monitor, mouse and speakers/microphone. Save on equipment cost, utility, and space. |
| Performance | Support High Quality 2048 x 1536 resolution |

Package Contents				Related Products

- 4-Port Audio KVM Switch			- TK-206i

- 4 Sets of Audio KVM Cables			- TK-209i

- Multi-Language User’s Guide			- TK-210K

- Rack Mount Kit

To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

### Sales: sales@trendware.com • Support: techsupport@trendware.com

Tech Support Hot Line: 1-310-626-6252

### Official Site: www.TRENDNET.com

# Text boxes

#### TK-403KR

4-Port Audio KVM Switch

TRENDnet’s TK-403KR 4-port KVM encompasses all your multimedia and multitasking needs into one cost effective solution.  Manage multiple PC’s effectively while enjoy audio-rich features with one set of monitor, keyboard, mouse, microphone, and speakers.

Audio KVM Switch Solution