Features

- Supports PC using KVM Switch’s Console Port or PC Port

- Extends keyboard, mouse, and monitor distances up to 500ft/152m

- Displays high VGA quality up to 1280 x 1024 resolution

- Provides local and remote console ports for dual simultaneous access

- Uses a single transmitter and receiver units connected via Ethernet cable

- Includes VGA adjustable Knob for optimal VGA quality

- Compliant with Cat5, Cat5E or Cat6 Ethernet cable

- Indicates data transmission and power through LEDs

- Works with standard 3-in-1 KVM switch cable

- Supports Windows 98SE/ME/2000/XP Operating Systems

- No Driver or Software Required

- 2-Year Warranty

Specifications

| Hardware |
| --- |
| Port Interface | PS/2 Keyboard: mini-din 6 pin Female PS/2 Mouse: mini-din 6 pin Female VGA: HDDB 15 pin Female |
| Cable Standards | Cat5, Cat5E or Cat6 |
| Supported OS | Windows 98SE/ME/2000/XP Linux, Unix and Netware |
| VGA Resolution | Up to 1280 x 1024 at 60 Hz |
| Power | 9V DC, 500mA |
| LEDs | Power, Data |
| KVM Cable | 60cm(2ft.) 3-in-1 KVM Cable |
| Dimension (L x W x H) | 110(L) x 85(W) x 33(H)mm ( 3.1 x 1.5 x 4.37 inches) |
| Weight | Transmitter: 142g (5oz.) Receiver: 128g (4.5oz.) |
| Temperature | Operation: 0(C~40(C (32(F~104(F) Storage: -5(C~70(C (23(F~158(F) |
| Humidity | 80% maximum |
| Certification | CE, FCC |
| Warranty | 2 Years |

Package Contents	Related Product

- TK-EX2 Transmitter	- TK-401R

- TK-EX2 Receiver	- TK-801R

- Multi-Language User’s Guide	- TK-802R

- Power Adapter DC9V, 500mA						- TK-1602R
- 2 ft. 3-in1 KVM Cable

To order please call: 888-326-6061 • Sales: sales@trendware.com

Support: techsupport@trendware.com • Tech Support Hotline: 1(310) 626-6252

Official Site: www.TRENDnet.com

# Text boxes

TK-EX2

CAT5 KVM Extension Kit

TRENDnet TK-EX2 Extension Kit provides a simple and affordable solution to control computer or KVM switch up to 500ft/152m away. Ideal for isolated server rooms, network operating centers, secure systems, or test benches where computers are inaccessible.  The TK-EX2 reduces equipment cost by utilizing standard CAT5 network cable to transmit keyboard, video, and mouse signals.

TK-EX2 Connection Solutions