Features

- IEEE 802.3af Power over Ethernet (PoE) Standard Compliant

- 16 x 10/100Mbps Auto-Negotiation and Auto-MDIX Fast Ethernet RJ45 Ports

- Built-in 8 PoE Ports (Port 1 ~ Port 8)

- Supports PoE Power Maximum 15.4 watts for each POE port

- Supports PoE Powered Device(PD) classification identify

- Full Wire-Speed Non-Blocking Reception and Transmission

- Store and Forward Switching Method

- 512K bytes RAM Data Buffer and 4K entries MAC Address Table

- Extensive Diagnostic LED’s on the Front Panel

- IEEE 802.3x Flow Control for Full-Duplex Mode; Back Pressure Flow Control for Half-Duplex Mode

- Proprietary Windows Based Management/Monitoring Utility (similar to SNMP Trap)

- Supports 802.1Q VLAN, Port-Based /IEEE 802.1p QoS

- Supports Port-Based Trunking (max. 4 groups on Port 9~16 only) and Port Mirroring

- Port Setting Function, Users can set each Port’s Availability, Speed, Duplex Mode, and Flow Control

- Easy configuration via Web browser

- Standard 19” (1U) Rack-Mount size (kit included)

- 5-Year Warranty

Specifications

| Hardware |
| --- |
| Standard | IEEE 802.3 10Base-T IEEE802.3u 100Base-TX IEEE 802.3af Power over Ethernet |
| Network Media | 10Mbps: Cat 3,4,5 Unshielded/Shielded/Screened Cable 100Mbps: Cat 5, 5E, 6 Unshielded/Shielded/Screened Cable |
| Protocol / Topology | CSMA/CD ; Star |
| Ports | 8 x 10/100Mbps Auto-MDIX POE Ports (1~8) 8 x 10/100Mbps Auto-MDIX Fast Ethernet Ports (9 ~16) |
| Data Transfer Rate | Ethernet: 10/20Mbps (half/full duplex) Fast Ethernet: 100/200Mbps (half/full duplex) |
| RAM Buffer / Filtering | 512 K Bytes / 4K entry per device |
| Power | 100~240VAC 50/60Hz, Internal Universal Switching Power |
| Diagnostic LEDs | Per Unit: Power, System Per Port: Link/Activity, Speed PoE: PoE Status (Port 1~8) |
| Power Consumption | 9 watts max (no PD Device connected) 130 watts max (8 x 15.4 watts PoE Device connected) |
| Temperature | Operating: 0( ~ 40( C (32( ~ 104(F); Storage: -10( ~ 70( C (14( ~ 158(F) |
| Humidity | 10%- 90% (non-condensing) |
| Dimensions | 440 x 210 x 44 mm (17.3 x 8.27x 1.73 inch) (W x H x D) |
| Weight | 3Kg (6.6 lb) |
| Certification | FCC, CE |
| PoE |
| Power over Ethernet | Up to 15.4 watts per Port; PD classification Identify PoE Over Current Protection; PoE Circuit Sorting Protection PoE Power on RJ-45 pin 3,6 for Power+ and pin 1,2 for Power- |

Power over Ethernet Solutions

Package Contents	Related Product

- TPE-S88						- TPE-101I

- Multi-Language User’s Guide	- TPE-102S

- Web-Smart Utility CD-ROM

- Power Supply

- Rack Mount Kit

To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

### Sales: sales@trendware.com • Support: techsupport@trendware.com

Tech Support Hot Line: 1-310-626-6252

### Official Site: www.TRENDNET.com

# Text boxes

16-Port 10/100Mbps Web Smart PoE Switch

TRENDnet’s TPE-S88 16-port Smart Switch integrates Power over Ethernet (PoE) and network management features into a cost effective and scalable solution. The TPE-S88 reduces equipment cost by delivering data and power over existing network cable infrastructure. The TPE-S88 offers advanced network management features such as VLAN and QoS to meet today’s secured network applications.

TPE-S88