Features

- Compliant with USB 1.1 and USB 2.0

- Built-in-one 10/100Mbps auto-MDIX fast Ethernet LAN Port and 2 USB 2.0 ports

- Provides Open mode and Account Mode

- Acts as DHCP client to locate IP from DHCP server or Auto-IP

- Provides FTP Server for remote access

- Automatic download or back up scheduling support

- Require to use with a USB 2.0 external disk drive, flash disk, or CD-ROM storage devices

- Provides windows or web based configuration

- Security with IP address filtering to ALLOW or DENY access

- Automatically self tests the circuits of Flash Memory, DRAM, Ethernet Port, and USB 2.0 Ports when power is on

- User account management

- Supports Windows 98/98(SE)/ME/NT/2000/XP and Linux SMB Operation System

- Web based administrative program stored into flash ROM of the server

- Supports UPnP for Windows XP

- Supports Network Time Protocol (NTP) to track data access

- 2-Year Warranty

Specifications

| Hardware |
| --- |
| Standard | IEEE 802.3, IEEE 802.3u, USB 1.1 and USB 2.0 |
| Port Interface | 1 x 10/100 RJ45 Connector (Auto-MDIX) 2 x USB 2.0 Ports 1 x Power Port |
| LEDs | Power, LAN, Mode |
| Buttons | Reset, Unmount |
| Power Consumption | 5VDC, 2.5A External Power Adapter |
| Dimensions (L x W x H) | 147 x 112 x 30 mm (5.79 x 4.41 x 1.18 in) |
| Weight | 196g (6.9 oz) |
| Temperature | Operation: 5(C ~ 50(C (41(F ~ 122(F) ; Storage: -20(C ~ 50(C (-4(F ~ 122(F) |
| Humidity | Operation: 10% - 90%; Storage: 5% - 95% (Non-Condensing) |
| Certification | CE, FCC |
| Firmware Specification |
| Standard | IEEE802.e, IEEE802.3u, USB2.0, USB1.1 |
| DHCP Client | Assigns IP address from DHCP server, Auto-IP |
| File System Type | Fat16 / Fat32 |
| Security | IP Filtering; User Account Management |

Package Contents							Related Product

- TS-U100								- TS-U200

- Quick Installation Guide

- CD-ROM (UG & Utility)

- Power Adapter (5V DC, 2.5 A)

To order please call: 888-326-6061 • Sales: sales@trendnet.com

Support: support@trendnet.com • Tech Support Hotline: 1(310) 626-6252

Official Site: www.trendnet.com

# Text boxes

Back View

TS-U100

USB 2.0 Network Storage Server

The TS-U100 Network File Server is a quick and easy economical solution that adds storage to your existing network.  It includes a Web based utility that manages storage access through IP filtering and supports network time protocol (NTP) to keep track of data access.  With a FTP Server service and hot-swappable features, the TS-U100 simplifies installation to meet large data demands.

Front View

Network Storage Solution with TS-U100