Features

- Compliant with Serial ATA II electrical specification 1.0

- Connects to 3.5” SATA II or SATA Hard Drives

- Compliant with USB 2.0 and 1.1 specifications

- Support USB 2.0 data transfer rate of up to 480Mbps

- Compliant with USB mass storage class, bulk-only transport specification

- Compliant with Windows 98SE/ME/2000/XP and Mac OS 8.6 or later Operation System

- Plug & Play and Easy Installation

- 2-Year Warranty

Specifications

| Hardware |
| --- |
| Standards | IEEE 802.3 / IEEE 802.3u USB 2.0, 1.1 |
| Interface | Power Switch 1 x USB 2.0 Type A port 1 x Internal 3.5” IDE/ 3.5” SATAII / SATA HD Bay (Hard Drive not included) |
| LED | Power |
| Power Consumption | 25 watts (min.) |
| Power | Input: AC 100~240V 50/60Hz 0.6A Output: 12V DC 2A |
| Dimensions | 225 x 140 x 37mm (8.9 x 5.5 x 1.5 in) |
| Weight | 600g (21oz) |
| Temperature | Operation: 0(C ~ 40(C (32(F ~ 104(F) Storage: -5(C ~ 55(C (23(F ~ 131(F) |
| Humidity | 85% ~ 90% (Non-Condensing) |
| Certification | CE, FCC |

Package Contents							Related Product

- TSE-IS401								- TS-I300

- Multi-Language Quick Installation Guide	- TS-I301W

- CD-ROM (User’s Guide)

- Power Adapter (12V DC, 2 A)

- USB Cable

To order please call: 888-326-6061 • Sales: sales@trendnet.com

Support: techsupport@trendnet.com • Tech Support Hotline: 1(866)845-3673

Official Site: www.TRENDnet.com

# Text boxes

USB 2.0 IDE/SATA Storage Enclosure

The 1-Bay USB 2.0 to IDE/SATA Enclosure allows users to use IDE or SATA hard drives over a USB 2.0 connection. .  It works with most 3.5” IDE  and SATA I and II hard drives. This device provides a simple, yet powerful data transfer and backup solution.

TSE-IS401 (v1.0R)