# FEATURES

- Intelligent Plug-N-Play USB 2.0 Mobile Docking Station with compact size design

- USB 2.0 standard and backwards compatible with USB 1.1 specifications

- Provide one upstream USB 2.0 port and three downstream USB 2.0 Hub ports

- Auto detects USB downstream port transmission speed with Over-Current protection

- Connect any external USB 2.0, 1.1 devices up to 480Mpbs transmission speed

- Built-in ready-to-use 10/100Mbps Fast Ethernet Adapter for network connection

- Built-in Modem port for Windows HyperTerminal and Dialup Networking applications

- Built-in Bi-directional Parallel Printer port, and It is also compliant with any USB printer

- Easy installation and compatible with Windows 98/98SE/ME/2000/XP

- Plug-N-Play feature for USB peripherals, connect or remove any peripherals without powering down the USB 2.0 Mobile Docking Station or the computer

- “Tiered star topology” supports up to 6 tiers (USB Hub) and 127 devices

- Easy to read LED Indicators for Power and USB 2.0 Hub ports for device status monitoring

- Use either USB bus-powered or self-powered with included AC/DC power adapter

- 1-Year Warranty

SPECIFICATIONS

| Computer Connection | 1 upstream USB 2.0 port |
| --- | --- |
| Interface | USB 2.0 Standard, 1.1 Specifications Compliant |
| USB Cable | 1 x 1.8 meters (6 ft) USB 2.0 AB type cable |
| Console Port Connectors | 1 x PS/2 Keyboard 6-pin mini DIN female 1 x PS/2 Mouse 6-pin mini DIN female 1 x RJ-45 10/100Mbps Fast Ethernet 1 x DB 9-pin RS-232 Standard Modem Serial port male 1 x DB 25-pin IEEE-1284 Standard Bi-directional Parallel Printer port female 1 x USB 2.0 / 1.1 type B upstream port 3 x USB 2.0 / 1.1 type A downstream ports |
| Driver Support | Windows 98/98SE/ME/2000/XP/2003 Server |
| LED Indicator | 1 x Power 3 x USB 2.0 Hub port |
| Power | USB bus-powered or included AC/DC Power Adapter 5V DC, 1.8 A (switching power adapter). 10 Watts max |
| USB-Power Consumption | 450mA ~ 500mA max |
| Dimensions / Weight | 118 x 64 x 25 mm (4.65 x 2.5 x 0.98 inches) / Appro. 117 g. (0.26lb.) |
| Operating/Storage Temperature | 0( ~ 70(C (32( ~158( F)/ 0( ~ 85(C (32( ~ 185( F) |
| Humidity | 0%~80%, Non-Condensing |
| Certification | FCC, CE |

TOP REASONS THE TU2-ET200 IS A LASTING TREND

| Integration Friendly | The USB 2.0 Mobile Docking Station allows you to connect eight different external peripherals to its ports simultaneously. It has a built-in 3-port USB 2.0 Hub, and a built-in ready-to-use USB-to-Ethernet Adapter |
| --- | --- |
| Flexible | Hot-Plug feature, connect or disconnect to the computer without powering down the computer |
| Cost Effective | Allows you to connect many external peripherals including modems, printers, scanners, digital cameras/camcorders, RW CD/DVD ROM drives, and external hard drives. Save on time, equipment cost, and space |
| Performance | This Intelligent high-speed device supports up to 480Mbps transmission data rate |

TU2-400		TU2-400	4-Port Hi-Speed USB Hub

TU2-ET100	Hi-Speed USB to Fast Ethernet Adapter

TU2-PCBUS	2-Port USB 2.0 CardBus Adapter

To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

Sales: sales@trendware.com • Support: techsupport@trendware.com

### www.TRENDNET.com

# Text boxes

Product Information

#### TU2-ET200

## USB 2.0 Mobile Docking Station

TRENDnet's TU2-ET200 is an intelligent external USB 2.0 device for connecting to USB enabled PCs or notebooks. This Intelligent high-speed, up to 480Mbps, USB 2.0 Mobile Docking Station allows you to connect eight different external peripherals to its ports simultaneously; one modem serial port, one printer port, one PS/2 keyboard, one PS/2 mouse, three high-speed USB 2.0 ports, and one built-in USB-to-Ethernet adapter port. With the Hot-Plug, the TU2-ET200 is the perfect choice for you to connect any external peripherals including modems, printers, scanners, digital cameras/camcorders, RW CD/DVD ROM, external hard drives, and up to 127 devices at home or in the office.

All-in-One

Solution for TU2-ET200

Back panel

Front panel