Features

- Supports M-JPEG Compression and Audio Monitoring

- Built-in RS-485 connectors for Pan & Tilt control device (additional Pan & Tilt control device required)

- Supports ActiveX Control for Internet Explorer and Java applet for Internet Explorer and Netscape Navigator

- Allows for Remote Access from Web Browser for Live Image Viewing and listening

- Supports TCP/IP networking, SMTP e-mail, HTTP and other Internet related protocols

- Supports Web Configuration with Password Protection

- Powerful Windows IPView  Application Software for multiple cameras monitoring, motion detection alerts, image capturing, and video recording (Windows 98/ME/2000/XP)

- Built-in I/O Ports to Trigger Alarm and Email Notification

- Broad Range of Applications for Monitoring Homes, Offices, Banks, Hospitals, and a Variety of Private and Public Monitoring

- 3-Year Warranty

Specifications

| Camera Specifications |  |
| --- | --- |
| Image Sensor | System |
| Sensor | 1/4” Color CMOS Sensor | CPU | ADMtek 5120 |
| Resolution | 640 x 480 pixel | SDRAM/Flash | 16MB/4MB |
| Lens | f :6.0mm F1.8 Lens (CS-Mount Standard, Replaceable) | OS | Linux |
|  |  | I/O & Control |
|  |  | Input | 1 set, 2 pin (photo relay; Active High: 9~40V DC; Dropout: 0 VDC) |
| Minimum Illumination | IR On: 2.5 lux IR Off: 2.5 lux |  |  |
|  |  | Output | 1 set, 2 pin (photo relay. Close circuit current: 70mA~100mA; 30Ohm. Open circuit voltage: 240VAC or 350VDC) |
| Audio |  |  |
| MIC Input | Internal MIC (mono) | RS-485 | Half Duplex (to control external pan/tilt device |
| Volume Control | Adjustable |  |  |
| Compression | ADPCM/PCM | Requirements |
| Video & Image |  | Memory Size | 512MB or above |
| Image Frame Rate | 30fps@CIF, QCIF, VGA | Intel Celeron 1.1GHz or above (Pentium 4 Recommend) VGA card resolution: 800 x 600 or above |
| Compression | M-JPEG |  |
| Resolution & Light Frequency | 176 x 144, 320 x 240, 640 x 480 Outdoor/Indoor/50Hz/60Hz | Physical/Environmental |
| Frame Rate Setting | 1, 3, 7, 12, 15, 25, 30 (Depends on video format) | Dimension | 180 x 83 x 47mm (7.1 x 3.3 x 1.9in.) |
|  |  | Weight | Camera: 247g (8.7oz.) Stand: 116g (4.1oz.) |
| Mirror Function | Vertical / Horizontal |  |  |
| Control | Yes (Brightness/ Contrast/ Saturation/Sharpness) | Stand Height | 128 mm (4.7 inches) |
|  |  | Power | 5VDC 2.5A External Power Adapter |
| Hardware Specifications |  |  |
| Communication | Consumption | 4.5 Watt max. |
| LAN | 10/100Mbps Auto-Sense, Auto-MDIX |  |  |
|  |  | Temperature | Operating: 5(C ~ 40(C (41(F ~ 104(F) Storage: -25(C ~ 50(C (-13(F ~ 122(F) |
| Protocol | HTTP, FTP< TCP/IP, UDP, ARP, ICMP, DHCP, PPPoE, DDNS, SMTP, UPnP |  |  |
|  |  | LED | Power: Blue Link/Active: Orange |
| Software |  |  |  |
| Browser | Internet Explorer 5.0 or above Netscape 6.0 or above | Humidity | 5% ~ 95% Non-Condensing |
| Application | IP View and Active X |  |  |
| Supported OS | Windows 98SE, ME,2000,XP | Safety Emissions | CE, FCC |

Package Contents							Related Product

- TV-IP201								- TV-IP100

- Utility CD-ROM							- TV-IP100W

- Multi-Language Quick Installation Guide 				- TV-IP201W

- RJ-45 Ethernet Cable						- TV-IP300

- Power Adapter (5V 2.5A)						- TV-IP300W

- TV-IP400

- TV-IP400W

To order please call: 888-326-6061   Sales: sales@trendnet.com

Support: support@trendnet.com   Tech Support Hotline: 888-777-1550

www.trendnet.com

# Text boxes

Internet Camera Server with Audio

TV-IP201 Internet audio Camera Server is the perfect device for remote monitoring and transmitting real-time events over the Internet. The TV-IP201 functions as a video/audio/surveillance camera allowing you to view live events with your web browser via Internet or Intranet. Up to 16 cameras can be remotely managed with the bundled IP View software. This Internet Camera Server has M-JPEG quality streaming video, automatic image capture, and event notification via e-mail, making it the ideal solution for Internet video broadcasting applications.

TV- IP201(v1.0R)

Network Solution for TV-IP201