## Features

- Built-in 4 x 10/100Mbps Auto-MDIX Ports

- Built-in 1 x 10/100Mbps WAN Port and 1 x USB 1.1 Compliant Print Server Port

- Supports Cable/DSL Modems with Dynamic IP, Static (Fixed) IP, PPPoE, PPTP, or L2TP Connection Types

- Compliant with Windows 95/98/ME/NT/2000/XP, Unix, and Mac System

- Supports TCP/IP Printing Protocol with Peer to Peer Printing Method

- Supports of up to 100 (IPSec, L2TP, PPTP) Pass-Through Sessions Simultaneously (when each VPN client connects to a different VPN endpoint)

- Website Access Restriction using URL Keywords (50 entries)

- Provides Virtual Servers (40 entries) and Services Type Control

- Provides Access Control with User Define Services Types (70 entries)

- Provides Static Routing, Dynamic DNS Service and Multi-DMZ

- ALGs (Application Level Gateways) with Special Application Support (6 entries) and UPnP (Universal Plug & Play) Support

- Supports Network Address Translation (NAT/NAPT) and Stateful Packet Inspection (SPI) Firewall

- Real-Time Email Alert and Logs (Outgoing, Access Control & DoS Attacks)

- Easy Web Browser Configuration and Remote Management

- Flash Memory for Firmware Upgrade and Save/Restore Router Configuration

- 5-Year Warranty

## Specifications

| Hardware |
| --- |
| Standards | IEEE 802.3 (10-Base T), 802.3u (100-Base TX) |
| Protocols | NAT, PPPoE, HTTP, DHCP, TCP/IP, UDP, PAP, CHAP, RIP1, RIP2, DDNS |
| WAN | 1 x 10/100Mbps Port (Internet) |
| LAN | 4 x 10/100Mbps Auto-MDIX Ports |
| Printer Port | 1 x USB 1.1 Port |
| LED Indicators | Unit: Power, Status, WAN LAN Ports: Link/Act, 100 |
| Power Adapter | 12V DC, 800mA |
| Dimensions (L x W x H) | 141 x 100 x 27 mm (5.5x 3.9 x 1.06 inches) |
| Weight | 0.36 kg (12.8 oz.) |
| Temperature | Operating: 0˚ to 40˚ C (32˚ to 104˚ F) Storage: -10˚ to 70˚ C (14˚ to 158˚ F) |
| Humidity | Operating: 0 % ~ 80 % (non-condensing) Storage: 0% ~ 95% (non-condensing) |
| Certifications | CE, VCCI |
| Router |
| Firewall | NAT Firewall, SPI Firewall |
| Security | URL Filter, Access Control, Password Protection, Email Alert and Logs |
| VPN Pass-Through | IPSec, PPTP, L2TP (100 Sessions) |
| Print Server |
| Protocol | TCP/IP |
| Printing Method | PTP (Peer-to-Peer) over TCP/IP, LPD |

### TOP REASONS THE TW100-BRF114U IS A LASTING TREND

| Easy Integration | With the built-in 10/100Mbps Switch, you can integrate this device to any Ethernet/Fast Ethernet Network |
| --- | --- |
| Cost-Effectiveness | Share the broadband Internet connection, saves router costs and account charges |
| Security | Firewall Protection keeps hackers out |
| Performance | Experience the high speed Internet access while reducing network traffic |

Product Information

TW100-BRF114	Cable/DSL 4-Port Firewall Router

TW100-BRV204	Cable/DSL VPN Firewall Router

TW100-BRV304	Cable/DSL Advanced VPN Firewall Router

TW100-S4W1CA	Cable/DSL Broadband Router /w 4-Port Switch

To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

Sales: sales@trendware.com • Support: techsupport@trendware.com

www.TRENDNET.com

# Text boxes

TW100-BRF114U

Cable/DSL 4-Port Firewall Router

w/ USB Print Server

TRENDnet's TW100-BRF114U 4-Port Cable/DSL Firewall Router with integrated USB Print Server allows users to easily and securely share an Internet connection, files, virtually all types of USB printers, and other resources. The router’s Stateful Packet Inspection Firewall (SPI) protects against popular Denial of Service attacks, while Multiple Web Patrol features allow parents and Network Administrators to restrict internet access based on clients' IP Addresses, Time/Date, URL Keywords, and Service Types. The TW100-BRF114U’s integrated USB Print Server allows users to transform a standalone USB Printer into a shared network resource for increased cost-savings and productivity. An intuitive web browser configuration makes configuring the TW100-BRF114U quick and easy.

Network Solution for TW100-BRF114U

Back Panel

Front Panel