## Features

- Built-in 3 x 10/100Mbps Auto-MDIX Ports

- Built-in 1 x 10/100Mbps WAN Port and 1 x 10/100Mbps DMZ Port

- Supports Cable/DSL Modems with Dynamic IP, Static (Fixed) IP, PPPoE, PPTP, or L2TP Connection Types

- Compliant with Windows 95/98/ME/NT/2000/XP, Unix, and Mac System

- Supports up to 70 IPSec Tunnels

- Supports 100 (IPSec, L2TP, PPTP) Pass-Through Sessions Simultaneously (when each VPN client connects to a different VPN endpoint)

- Supports PPTP 1 Server and 10 Client (Microsoft VPN) VPN Connections

- Website Access Restriction using URL Keywords (50 entries) and Special Application Access

- Provides Virtual Servers(Port Forwarding) and Services Type Control with up to 60 Firewall Rules

- Provides Access Control with user define Services Types (70 entries)

- Provides Static Routing, Dynamic DNS Service, Hardware DMZ, and Software Multi-DMZ

- ALGs (Application Level Gateways) and Special Application Support (6 entries) or smooth on-line Gaming behind a Firewall and UPnP (Universal Plug & Play) Support

- Supports Network Address Translation (NAT/NAPT) and Stateful Packet Inspection (SPI) Firewall

- Real-Time Email Alert and Logs (Incoming, Outgoing, System, and VPN)

- Easy Web Browser (HTTP) Configuration and Remote Management (HTTPS)

- Flash Memory for Firmware Upgrade and Save/Restore Router Configuration

- 5-Year Warranty

## Specifications

| Hardware |
| --- |
| Standards | IEEE 802.3 (10-Base T), 802.3u (100-Base TX) |
| Protocols | NAT, PPPoE, NTP, SMTP, HTTP, TFTP, DHCP, TCP/IP, PAP, CHAP, RIP1, DDNS |
| WAN | 1 x 10/100Mbps Port (Internet) |
| LAN | 3 x 10/100Mbps Auto-MDIX Ports |
| DMZ | 1 x 10/100Mbps Auto-MDIX Port |
| LED Indicators | Unit: Power, Status, PPPoE LAN Ports/DMZ Port: Link/Act, 100 |
| Power Adapter | 12V DC, 800mA |
| Dimensions (L x W x H) | 170 x 147 x 27 mm (6.7x 5.8 x 1.06 inches) |
| Weight | 0.6 kg ( 20.8 oz.) |
| Temperature | Operating: 0˚ to 40˚ C (32˚ to 104˚ F) Storage: -10˚ to 70˚ C (14˚ to 158˚ F) |
| Humidity | Operating: 0 % ~ 80 % (non-condensing) Storage: 0% ~ 95% (non-condensing) |
| Certifications | FCC, CE, VCCI |
| Router |
| Firewall | NAT Firewall, SPI Firewall |
| Security | URL Filter, Access Control, Password Protection, Email Alert and Logs |
| VPN (IPSec) | MD5-HMAC/SHA1-HMAC Authentication, DES-CBC, 3DES-CBC Encryption, Internet Key Exchange, Manual Key Negotiation |
| VPN Tunnels | 70 (IPSec), 10 (PPTP) |
| VPN Pass-Through | IPSec, PPTP, L2TP (100 Sessions) |

### TOP REASONS THE TW100-BRV304 IS A LASTING TREND

| Easy Integration | With the built-in 10/100Mbps Switch, you can integrate this device to any Ethernet/Fast Ethernet Network |
| --- | --- |
| Cost-Effectiveness | Share the broadband Internet connection, saves router costs and account charges |
| Security | Firewall protection keeps hackers out |
| Performance | Experience the high speed Internet access while reducing network traffic |

Product Information

TW100-BRV204	Cable/DSL VPN Firewall Router

TW100-BRV304	Cable/DSL Advanced VPN Firewall Router

TW100-BRF114	Cable/DSL Firewall Router

TW100-S4W1CA	Cable/DSL Broadband Router

To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

Sales: sales@trendware.com • Support: techsupport@trendware.com

www.TRENDNET.com

# Text boxes

TW100-BRV304 (v2)

Cable/DSL Advanced VPN Firewall Router

TRENDnet’s TW100-BRV304 Cable/DSL Advanced VPN Firewall Router provides small business users advanced broadband security with a Stateful Packet Inspection Firewall (SPI) that filters traffic down to the packet level and incorporates protection against popular hacker attacks such as Denial of Service (DoS) attempts. It includes VPN encryption with support for up to 70 simultaneous VPN tunnels via client pc-to-endpoint or endpoint-to-endpoint configuration. To allow direct access to a web server or PC around the firewall the router includes a dedicated DMZ port. Installation and VPN Set-up is quick and easy with the help of the install wizard. The new VPN Firewall family delivers advanced security at an affordable price.

Network Solution for TW100-BRV304

Front Panel

Back Panel