## Features

- Supports Cable/DSL Modem with Dynamic IP, Fixed IP, PPPoE or PPTP Connection Types

- Compliant with Windows 95/98/NT/2000/XP, Linux and Mac Operating Systems

- Provides NAT (Network Address Port Translation) Firewall

- Supports Virtual Servers (Port Forwarding) and DMZ

- Supports Client Filtering by Date/Time (10 Entries and Special Applications Filter (10 Entries)

- Supports MAC Address Control to Allow or Deny Access (32 Entries)

- Supports DNS (Domain Name System) Account for Server Mapping and Dynamic DNS Service

- Supports IPSec and PPTP VPN Pass-Through (when each VPN client connects to a different VPN

endpoint)

- Include Static Route Feature

- Supports UPnP (Universal Plug & Play)

- Built-in 4-Port 10/100Mbps Auto-MDIX Switch

- DHCP Server Supports up to 253 Users

- Easy Web Browser Configuration and Remote Management

- Flash Memory for Firmware Upgrade and Save/Restore Router Configuration

Specifications

| Hardware |
| --- |
| Standards | IEEE 802.3 10Base-T, IEEE 802.3u 100Base-TX, ANSI/IEEE 802.3 Auto-Negotiation |
| Network Protocols | TCP/IP, NAT, PPPoE, UPnP, HTTP, DHCP Server/Client, SNTP |
| Protocol / Topology | (CSMA/CD) / Star |
| WAN | 1 x 10/100Mbps Port (Internet) |
| LAN | 4 x 10/100Mbps Auto-MDIX Ports |
| Cabling | Ethernet: Cat. 3, 4, 5, UTP EIA/ITA-568 100 Ohms, 100meters max Fast Ethernet: Cat. 5, UTP EIA/TIA-568 100 Ohms, 100meters max |
| Data Transfer Rate | Ethernet : 10Mbps/20Mbps (Half-Duplex/Full-Duplex) Fast Ethernet: 100Mbps/200Mbps (Half-Duplex/Full-Duplex) |
| LED Indicator | Power, System, WAN: Link/ACT 100M, LAN: Link/ACT 100M |
| Power Consumption | 7watts. (max) |
| Dimension (L x W x H) | 165 x 114 x 44mm (6.5 x 4.5 x 1.7 inches) |
| Weight | 236g (0.52 lb) |
| Temperature | Operating: 0ﾟ ~ 40ﾟC ( 32ﾟ ~ 104ﾟF) Storage: -10ﾟ ~ 70ﾟC (14ﾟ ~ 158ﾟF) |
| Humidity | Operating: 10% ~ 90% RH Storage: 5% ~ 90% RH (Non-Condensing) |
| Power Adapter | 7.5V DC, 1A |
| Certification | FCC & CE |
| Warranty | 5 Years |
| Router |
| Connection Type | Dynamic IP, Static (Fixed) IP, PPPoE, PPTP |
| Firewall | NAT |
| Management | Web Browser Configuration & Remote Management |

### TOP REASONS THE TW100-S4W1CA IS A LASTING TREND

| Easy Integration | Built-in 4-port 10/100Mbps Switch, you can integrate this device to any Ethernet/Fast Ethernet Network |
| --- | --- |
| Cost-Effectiveness | Saves router costs and on-line charges |
| Security | Added firewall protection keeps hackers out |
| Performance | Up to 80Mbps throughput between Internet (WAN) and local area network (LAN) |

PRODUCT		TW100-S4W1CA	Cable/DSL 4-Port Broadband Router

INFORMATION	TW100-BRF114	Cable/DSL 4-Port Firewall Router

TW100-BRV304	Cable/DSL 4-Port Firewall Router

TW100-BRV304	Cable/DSL 4-Port Advanced VPN Firewall Router

To order please call: 888-326-6061

3135 Kashiwa Street • Torrance, CA 90505 • (310) 891-1100 • Fax: (310) 891-1111

Sales: sales@trendware.com • Support: techsupport@trendware.com

www.TRENDNET.com

# Text boxes

Cable/DSL 4-Port Broadband Router

TRENDnet’s TW100-S4W1CA 4-port Cable/DSL Broadband router provides the easiest and securest way to share your high-speed Cable/xDSL Internet connection. It has four 10/100Mbps half/full duplex switch ports that directly connect to workstations or uplink to another hub or switch. The TW100-S4W1CA also functions as a firewall for your PC, protecting your computer from hackers. It allows up to 253 users to access the Internet using a single ISP account. By sharing just one TW100-S4W1CA, one IP address, and one Cable/xDSL modem, dozens of network users can surf the Internet simultaneously. TRENDnet’s Cable/DSL Modem Internet Station is a feature-rich product that provides cost-effective functionality and an easy configuration.

TW100-S4W1CA

(Version F)

Front Panel

Back Panel

Network Solution for TW100-S4W1CA